## Slide 1: Team 505: SAE Hybrid Vehicle Battery Box and Battery Management System
28-March-19

## Slide 2: Team Introductions
Thomas O’Neill
Project Manager
Christopher Fishman
BMS Engineer
William Pisani
Cooling Specialist
Christian Gaya
Battery Engineer
Raymond Klouda
Impact Engineer

## Slide 3: Sponsor and Advisor
Sponsor Liaison
Michael Hays
Technical Specialist at Cummins
Academic Advisor
William Oats, Ph.D.
FAMU-FSU College of Engineering Professor
Christian Gaya

## Slide 4: Objective
Design a battery box and battery management system (BMS) for the SAE hybrid vehicle competition team.
Christian Gaya

## Slide 5: Customer Needs
Interpreted Needs
  Design a program that takes in parameters about motors and outputs information about the battery system.
  The battery box protects the battery, prevents overheating, and avoids environmental impact.
  A small-scale prototype should be created with proper specifications.
  BMS maintains charge control, cell balancing, and monitors power input and output.
  Battery system for a momentary high-torque boost should be a focal point of the BMS system.
  The battery box and BMS both adhere to SAE competition guidelines.
Christian Gaya

## Slide 6: Functional Decomp
Battery System
Battery Containment
Battery Management System
Support
Monitor
Integrate
Configure
Control
External Forces
Battery Load
Vehicle Chassis
Battery Layout
Temperature
Control
Charge
Current Flow
Voltage Level
Power Output
Batteries
Temperature
Christian Gaya

## Slide 7: Functional Decomp
Christian Gaya
Battery Containment
Support
Integrate
Configure
Control
External Forces
Battery Load
Vehicle Chassis
Battery Layout
Temperature

## Slide 8: Functional Decomp
Christian Gaya
Battery System
Battery Containment
Battery Management System
Support
Monitor
Integrate
Configure
Control
External Forces
Battery Load
Vehicle Chassis
Battery Layout
Temperature
Control
Charge
Current Flow
Voltage Level
Power Output
Batteries
Temperature

## Slide 9: Functional Decomp
Christian Gaya
Battery Management System
Monitor
Control
Charge
Current Flow
Voltage Level
Power Output
Batteries
Temperature

## Slide 10: Concept Generation
Biomimicry
    Analytically applied our problem to nature and brainstormed nature's own solutions.
Anti-Problem
    Project problems were reversed, and possible solutions to these anti-problems were found.
Morphological Chart
    Lists functions and various mechanisms that can be used to perform the functions listed.
    These Included the ideas we found from biomimicry, anti-problems, and the customer needs.
    Lines were used to connect the rows and columns of the chart. Each line represented a different possible concept.
10
Raymond Klouda

## Slide 11: Concept Selection
House of Quality
  Compared customer requirements to engineering characteristics (evaluation criteria).
  Generated the proper evaluation criteria for the Pugh charts.
Pugh Charts
  Determined the most important design concepts based on the evaluation criteria through comparing each concept to a datum.
Analytical Hierarchy Process
  A more “Mathy” way to make a decision compared to Pugh Charts.
  Equations were used for each evaluation criteria and design concept.
Raymond Klouda

## Slide 12: Finite Element Analysis (FEA)
Thomas O’Neill
FEA was used to aid in material selection and mounting of the battery box.
The following thicknesses were tested for impact strength and G-loading:
  0.25 inches,
  0.1875 inches, and
  0.125 inches.
The results showed that a thickness of 0.125 inches was sufficient for the battery box.

## Slide 13: Thermal Analysis
Thomas O’Neill
Thermal analysis was performed to maintain safe operating conditions.
The following were calculated:
  Velocity profile,
  Energy consumption,
  Battery operating temperature, and
  Volumetric flow of a fan.

## Slide 14: Velocity Profile
Thomas O’Neill
Chart: NHMS Velocity Profile
An velocity profile estimation was found using average track speed data and vehicle specifications.

## Slide 15: Embodiment
Complete design of scale model.

## Slide 16
Thomas O’Neill

## Slide 17
Thomas O’Neill

## Slide 18
Thomas O’Neill

## Slide 19
Thomas O’Neill

## Slide 20
Thomas O’Neill

## Slide 21: Manufacturing
Christopher Fishman

## Slide 22: Electrical Components Assembly
Nissan Leaf Modules and Orion Jr. BMS were chosen.
  Components were integrated by following manufacturers specifications for series battery configuration.
The BMS requires 9-60V for operating power.
  2 supplies were used: battery pack and 12 VDC power supply.
  12 VDC power supply was used to emulate a car alternator.
Christopher Fishman

## Slide 23: Electrical Schematic
Christopher Fishman

## Slide 24
Manufacturing Drawings
Raymond Klouda

## Slide 25
Manufacturing Drawings
Raymond Klouda

## Slide 26: Testing
Christian Gaya

## Slide 27: Testing Electrical Systems
Discharge characteristics of Nissan Leaf Modules
  Voltage change over time during constant-current discharge.
  Charge life for an individual module was estimated.
  Charge life data was extrapolated for a full-scale battery pack.
Time required to bring modules to full-charge from different voltage levels of the modules
  After being discharged, the batteries were connected to a charging circuit and the results were monitored.
Temperature monitors
  Thermistors were tested in controlled-climate conditions to ensure accuracy.
Christian Gaya

## Slide 28: Testing the Battery Box
Thomas O’Neill

## Slide 29: Testing the Battery Box
Thomas O’Neill

## Slide 30: Most Important Points
Small-scale model is functional.
The battery box adequately protects the components.
The battery system meets SAE competition guidelines.
Worth considering alternate battery sources other than Nissan Leaf modules. Ex. Battery pack constructed from 18650 cells.
Christopher Fishman

## Slide 31: Lessons Learned
Small vendors can be difficult when it comes to meeting deadlines.
Thorough understanding of the functionality of your components is critical to proper implementation; always read through manuals and documentation.
Expect delays beyond the delays that are already accounted for.
Christopher Fishman

## Slide 32: Reference
Motors. (n.d.). Retrieved February, 2019, from http://www.evwest.com/catalog/index.php?cPath=8
Fuel Economy Retrieved February, 2019, from https://www.fueleconomy.gov/feg/hybridtech.shtml.
800hp Electric Pickup Retrieved February, 2018, from https://www.hardworkingtrucks.com/rivian-reveals-chassis-of-800-hp-electric-pickup/
2019 Formula SAE Rules. Retrieved February, 2019, from https://formula-hybrid.org/wp-content/uploads/2019-Formula-Hybrid-Rules-Rev-0.pdf

## Slide 33: Questions

## Slide 34: Backup Slides

## Slide 35: Functional Decomp Backup

## Slide 36
Question/Prompt ​ | Customer Statement ​ | Interpreted Need ​
Should we build a battery box specific to the current SAE hybrid vehicle? ​ | I want to be able to provide parameters about the battery that the box is holding and get values returned about the size of the box. ​ | A program should take parameters about a battery and output parameters about a battery box. ​
Should a physical model of the battery box be built? ​ | The main item I'm looking for is the program that will give me values based on the battery. ​ | The main item I'm looking for is the program that will give me values based on the battery. ​
What should the battery box protect from? ​ | The container should be waterproof, thermally insulated,and environmentally sustainable. ​ | The battery box protects the battery. Thebattery box prevents overheating of the battery. The battery box does notnegatively impact the environment. ​
What should the BMS do? ​ | The BMS will maintain charge control and cell balancing of thebattery in a safe and efficient manner while also monitoring power input and output. ​ | BMS maintains charge control, cell balancing, and monitors power input and output. ​
What battery are we using to create a BMS for? ​ | Decide on a series of parallel battery. Whichever work best for the motor that is being used in the vehicle. ​ | Battery system for a momentary high-torque boost should be focal point of the BMS system ​
Should we investigate building our own battery orbuying one off the shelf? ​ | Creating your own battery would be very difficult. I recommendbuying one off the shelf and using that to create a BMS. ​ | Battery will be purchased. ​
Do you think there are any restrictions to the battery box and BMS? ​ | The SAE rulebook for the competition should contain all details about how the vehicles must be built. ​ | The battery box and BMS both must adhere to SAE competition guidelines. ​
Customer Needs Chart

## Slide 38: Concept Selection Backup

## Slide 39
Function​ | Option 1​ | Option 2​ | Option 3​ | Option 4​
Box Shape​ | Cube​ | Rectangle​ | Cross​ | T-Shape​
Box Cooling​ | Liquid cooling​ | Aircooling (ventilation)​ | Fans​ | ​
Box Waterproofing​ | Rubber seals​ | Water diversion​ | Silicon Sealant​ | Vacuum Sealed​
Box Mounting​ | Integrated into chassis​ | Bolted into chassis​ | ​ | ​
Energy Storage Device​ | Individual ion-cells​ | Purchase off shelf​ | Capacitor​ | ​
Energy Storage Device Wiring​ | Series​ | Parallel​ | Both series and parallel​ | ​
BMS Measurements​ | Current​ | Voltage​ | Temperature​ | All measurements​
Current Type​ | AC​ | DC​ | ​ | ​
Charging Device​ | Wall power​ | Solar​ | Regeneration​ | ​
Morphological Chart

## Slide 40
Comparison Matrix

## Slide 41
House of Quality

## Slide 42
Nine-Design Pugh Chart

## Slide 43
Five-Design Pugh Chart

## Slide 44
Analytical Hierarchy Process

## Slide 45
Analytical Hierarchy Process Normalized

## Slide 46
Analytical Hierarchy Process (cont.)

## Slide 47
Analytical Hierarchy Process (cont.)

## Slide 48
Air intake Hydro shield
Acts as a prefilter
Rejects any particle ~0.005”
Inexpensive
Easy to install

## Slide 49: Detailed Math Backup

## Slide 52: Standard Shapes
Summary Box
Text box 1
Outlined Text Box

## Slide 53: Approved Logos

## Slide 54: Color Palette

## Slide 55: APA Tables
Category 1 | Category 2 | Category 3 | Category 4 | Category 5
Item 1 |  |  |  | 
Item 2 |  |  |  | 
Item 3 |  |  |  | 
Item 4 |  |  |  | 
 | Category 2 |  |  | Category 3 | 
Category 1 | subcategory 1 | subcategory 2 |  | subcategory 1 | subcategory 2
Item 1 |  |  |  |  | 
Item 2 |  |  |  |  | 
Item 3 |  |  |  |  | 
Item 4 |  |  |  |  |