## Slide 1
Team 501: Powder Recovery for Metal Additive Manufacturing
Arlan Ohrt
Kevin Richter
Vincent Giannetti
Noah Tipton
Joshua Dorfman
March 10th, 2020

## Slide 2: Team Introductions
Arlan Ohrt
Project/Systems Engineer
Kevin Richter
Field
Engineer
Noah Tipton
Design
Engineer
Vincent Giannetti
Manufacturing
Engineer
Joshua Dorfman
Field
Engineer

## Slide 3
Sponsor – Air Force Research Labs (AFRL)
AFRL/RWMW – Ordnance Division, Damage Mechanisms Branch (Eglin Air Force Base)
  A global leader in advancing weapons science and technology
Specific Contact - Dr. Philip Flater
  Lead for the metal additive manufacturing lab at AFRL/RWMW
Joshua Dorfman

## Slide 4
Project Description
The objective of this project is to design a device which increases the amount of recovered steel powder in a metal additive manufacturing process. This device should be compatible with existing hardware and processes while ensuring the safety of the operators.
Joshua Dorfman

## Slide 5
Project Key Goals and Customer Needs
The objective of this project is to design a device which increases the amount of recovered steel powder in a metal additive manufacturing process. This device should be compatible with existing hardware and processes while ensuring the safety of the operators.
Joshua Dorfman
Increase amount of recovered steel powder
Be compatible with existing hardware and processes
Ensure operators safety

## Slide 6
The Scope of the Project
Joshua Dorfman
Recycle
Recover
Remove

## Slide 7
The Scope of the Project
Joshua Dorfman
Recycle
Recover
Remove
Sponsor
Design Team

## Slide 8
The Scope of the Project
Joshua Dorfman
Recycle
Recover
Remove
Sponsor
Design Team

## Slide 9
Project Background – Metal Additive Manufacturing
Laser Powder Bed Fusion (LPBF):
Powder Distributed in an Even Layer
Laser Traces Layer Path to “Fuse” Material Together
AFRL’s operating 3D printer is the 3D Systems ProX 300
This process results in a large amount of “unfused” powder. This powder should be recycled.
Joshua Dorfman

## Slide 10
Project Background – Metal Additive Manufacturing
Laser Powder Bed Fusion (LPBF):
Powder Distributed in an Even Layer
Laser Traces Layer Path to “Fuse” Material Together
Joshua Dorfman
This process results in a large amount of “unfused” powder. This powder should be recycled.

## Slide 11
Project Background – Metal Additive Manufacturing
Roller
Overflow
Build Plate
Powder Supply
Joshua Dorfman

## Slide 12
Project Background – The Metal Used
Joshua Dorfman
General Info:
Purchasable from 3D Systems
Particle Size: 10 – 15 μm (Paper thickness is ~ 100 μm)
Martensitic Steel (Magnetic)
17– 4PH Stainless Steel: 17% Chromium, 4% Nickel, Precipitation Hardening

## Slide 13
Project Background – The Metal Used
Joshua Dorfman
General Info:
Purchasable from 3D Systems
Particle Size: 10 – 15 μm (Paper thickness is ~ 100 μm)
Martensitic Steel (Magnetic)
17– 4PH Stainless Steel: 17% Chromium, 4% Nickel, Precipitation Hardening

## Slide 14
Noah Tipton
Powder Recovery Stages

## Slide 15
Noah Tipton
Project Background – Powder Recovery Stages
“Wet Vac Stage”
“Air Powered Stage”
“Built In Stage”

## Slide 16
Project Background – Powder Recovery Stages
Stage 1 – “Built In Stage”
Built in recovery system
  Vacuum
  Overflow Reservoir
Operation
  Sealed chamber
  Glove to operate vacuum
Substantial Powder Recovery
Noah Tipton

## Slide 17
Project Background – Powder Recovery Stages
Stage 2 – “Wet Vac Stage”
Removing the part
  Pass the build plate out
Operation
  Use powered air purifying respirator (PAPR)
  Open door and remove part
  Use Ruwac NA35 Immersion Vacuum
No Powder Recovery
Noah Tipton

## Slide 18
Project Background – Powder Recovery Stages
Stage 3 – “Air Powered Stage”
Sandblasting cabinet
Operation
  Place part inside the enclosure
  Use compressed air to remove residual powder
No Powder Recovery
Noah Tipton

## Slide 19
Noah Tipton
Project Background – Powder Recovery Stages
“Wet Vac Stage”
“Air Powered Stage”
“Built In Stage”
Substantial Powder Recovery
No Powder Recovery
No Powder Recovery
“Our System”
Substantial Powder Recovery

## Slide 20
Noah Tipton
Project Background – Powder Recovery Stages
“Wet Vac Stage”
“Air Powered Stage”
“Built In Stage”
Substantial Powder Recovery
No Powder Recovery
No Powder Recovery
“Our System”
Substantial Powder Recovery

## Slide 21
Functional Decomposition with Targets and Metrics
Noah Tipton
1) Volume
2) Force
Up to Eglin AFB safety standards
Particle Size
1) 250 x 250 x 300 mm
2) 356 N
Passes through 75 μm mesh
Pass Bioenvironmental Engineering Flight (BEF) air test
Metric
Target
Mass
Mass
Greater than 0 grams of separated powder in container
Recover Powder
Manage Powder
Support the Part
Inhibit Powder
Separates powder from the part
Transports powder
to a container
Isolate the powder
from user
Hold the part
in the area
Prevents powder contamination

## Slide 22
Build Plate and Part
Fasteners
Vibrator
New System
Noah Tipton

## Slide 23
New System – Structural Analysis
Noah Tipton
* CREO Von Mises
σMax* ≈ 315 psi
σy ≈ 40,000 psi
σMax *≈ 915 psi
σy ≈ 40,000 psi
τMax ≈ 157 psi
τFail ≈ τTresca ≈ 20 ksi
σMax*≈ 300 psi
σy ≈ 47,000 psi

## Slide 24
New System – Structural Analysis
What About Safety?
Noah Tipton
* CREO Von Mises
σMax* ≈ 315 psi
σy ≈ 40,000 psi
σMax *≈ 915 psi
σy ≈ 40,000 psi
τMax ≈ 157 psi
τFail ≈ τTresca ≈ 20,000 psi
σMax*≈ 300 psi
σy ≈ 47,000 psi

## Slide 25
Build Plate and Part
Fasteners
Vibrator
New System
What About Safety?
Noah Tipton

## Slide 26
Barrier Needed to Control Powder
New System
What About Safety?
BADBOY Blaster
Clamshell Design
Fits Design Well
Industrial Quality
Noah Tipton

## Slide 27
Barrier Needed to Control Powder
Chosen Barrier
What About Safety?
BADBOY Blaster
Clamshell Design
Fits Design Well
Industrial Quality
Noah Tipton
AFRL is Familiar with BADBOY’s Quality

## Slide 28
Chosen Barrier
BADBOY Blaster
Clamshell Design
Fits Design Well
Industrial Quality
Noah Tipton
AFRL is Familiar with BADBOY’s Quality

## Slide 29
Lessons Learned
Arlan Ohrt

## Slide 30
Initial Design Lessons Learned
Arlan Ohrt
Three Mistakes
Top Bar Fasteners
Vibrator Fasteners
Mounting Plate
Top Bar Fasteners
Problem
Reason
Solution
Fasteners were to short
Supplier CAD was not accurate
Ordered longer fasteners

## Slide 31
Initial Design Lessons Learned
Arlan Ohrt
Three Mistakes
Top Bar Fasteners
Vibrator Fasteners
Mounting Plate
Top Bar Fasteners
Problem
Reason
Solution
Fasteners were to short
Supplier CAD was not accurate
Ordered longer fasteners

## Slide 32
Initial Design Lessons Learned
Arlan Ohrt
Vibrator Fasteners
Problem
Reason
Solution
Fasteners were to short
Supplier CAD was not accurate
Ordered longer fasteners

## Slide 33
Initial Design Lessons Learned
Arlan Ohrt
Mounting Plate
Problem
Reason
Solution
Two holes did not line up
Machining mistake
Slotted the holes so they could be used

## Slide 34
Validation
Flour: 25 – 400 μm
75 μm Mesh
Arlan Ohrt
Scaled 4x
Printed Test Parts

## Slide 35
Validation
Arlan Ohrt
Scaled 4x
Printed Test Parts

## Slide 36
Validation
Arlan Ohrt
Printed Test Parts
Scaled 4x

## Slide 37
Budget
Arlan Ohrt
Enclosure
$8,000
$4,000
$2,000
$6,000
Design
$2,000
$1,000
$500
$1,500

## Slide 38
Design
$2,000
$1,000
$500
$1,500
Enclosure
$8,000
$4,000
$2,000
$6,000
Budget
Arlan Ohrt
$3,500
$1,100

## Slide 39
Design Budget
Arlan Ohrt
Structure
Build Plate Holder
Pneumatics
Suspension
$2,000
$1,000
$500
$1,500
$220
$243
$292
$345
$1,100

## Slide 40
Title Slide Background - https://www.materialise.com/en/blog/when-how-and-where-of-metal-3d-printing
Recycle - https://www.recycling.com/wp-content/uploads/recycling%20symbols/black/Black%20Recycling%20Symbol%20%28U%2b267B%29.png
3D Systems – https://www.3dsystems.com/3d-printers/prox-dmp-300/specifications
LPBF Demo GIF - https://thescopepopculturescience.blogspot.com/2015_01_01_archive.html
Stainless Steel Properties - https://www.3dsystems.com/materials/metal
nTopology – https://ntopology.com/
PAPR – https://images-na.ssl-images-amazon.com/images/I/4125zPcBPNL.jpg
Sandblaster - https://badboyblasters.com/product/abrasive-media-sand-blaster-bb1050led-bvr-pr-hv-fl-2/
AFRL Sign - https://news.wfsu.org/post/eglin-air-force-base-ready-adjust-hiring-freeze
Electric Vibrator - https://www.mcmaster.com/5808k61
Dampeners - https://www.mcmaster.com/29895t54 , https://www.mcmaster.com/9241k44
Flour - https://sugarandsparrow.com/homemade-cake-flour-recipe/
References

## Slide 41
Team 501: Powder Recovery for Metal Additive Manufacturing
Arlan Ohrt
Kevin Richter
Vincent Giannetti
Noah Tipton
Joshua Dorfman
March 10th, 2020

## Slide 42
Return
Backup Slides
Functional Decomposition
Group Member Contact
nTopology
Precipitation Hardening Explained
17- 4PH Material
3D Systems Printer Specs

## Slide 43
Return

## Slide 44
Return

## Slide 45
Group Contact
Return
Arlan Ohrt
ago16b@my.fsu.edu
Kevin Richter
kr15@my.fsu.edu
Noah Tipton
nrt15@my.fsu.edu
Vincent Giannetti
vjg15b@my.fsu.edu
Joshua Dorfman
jd16s@my.fsu.edu

## Slide 46
Functional Decomposition
Recover Powder
Manage Powder
Holds the part in the area
Transports powder to a container
Separates powder from the part
Insulates the user from powder
Prevents powder contamination
Support the Part
Inhibit Powder
Return

## Slide 47
Precipitation Hardening Explained
The strength and hardness of some materials can be increased by the formation of very small particles
This is done through heat treatments
It is called “Precipitation Hardening” because the process results in very small particles, called “Precipitates”
This works because precipitates help block dislocation motion, which is an important aspect of a materials failure and properties
Return
http://www.engineeringenotes.com/metallurgy/age-hardening-treatment/age-hardening-treatment-of-metals-metallurgy/26376

## Slide 48
17- 4PH Stainless Steel
Return
https://www.3dsystems.com/sites/default/files/2017-06/3D-Systems_17-4_PH_%28B%29_DMP_DATASHEET_US_A4_2017.06.21_WEB.pdf

## Slide 49
Arlan Ohrt

## Slide 50: Standard Shapes
Summary Box
Text box 1
Outlined Text Box

## Slide 51: Approved Logos

## Slide 52: Color Palette

## Slide 53: APA Tables
Category 1 | Category 2 | Category 3 | Category 4 | Category 5
Item 1 |  |  |  | 
Item 2 |  |  |  | 
Item 3 |  |  |  | 
Item 4 |  |  |  | 
 | Category 2 |  |  | Category 3 | 
Category 1 | subcategory 1 | subcategory 2 |  | subcategory 1 | subcategory 2
Item 1 |  |  |  |  | 
Item 2 |  |  |  |  | 
Item 3 |  |  |  |  | 
Item 4 |  |  |  |  |