## Slide 1: NASA Self-Leveling System
Team 516:
Stephen Brown
James Evans
Dalton LeClair
Jake Seaman
Parker Stensrud
EML 4552

## Slide 2: Team Introductions
Stephen Brown
Materials Engineer
James Evans
Design Engineer
Dalton LeClair
Test
Engineer
Jake Seaman
Systems Engineer
Parker Stensrud
Controls Engineer
Jake Seaman

## Slide 3: Sponsor and Advisor
Jake Seaman
Faculty Advisor
Dr. Dorr Campbell
FAMU-FSU College of Engineering
Project Sponsor
Rachel McCauley
NASA Marshall Space Flight Center

## Slide 4
Jake Seaman
Project Background

## Slide 5: Project Scope
Jake Seaman
The objective of our project is to provide a level working environment for the astronauts aboard the lunar lander.

## Slide 6
Jake Seaman

## Slide 7
Leveling Capabilities up to 12-Degree Slope
Supports 14-16 Metric Tons
Level Within an Hour
Reusability
Project Goals
Jake Seaman

## Slide 8: Concept Development
Jake Seaman

## Slide 9: Concept Ideation
Jake Seaman

## Slide 10: Developing Concepts
Brainstormed 100 concepts
Narrowed concepts down into 5 medium fidelity and 3 high fidelity
Processed medium and high-fidelity concepts
Linear Actuator ranked highest
Jake Seaman

## Slide 11: Initial Concept
Jake Seaman

## Slide 12: Prototype Breakdown
James Evans

## Slide 13: Prototype Critical Numbers
James Evans
Impact Force: 29.12 lbf
Stress on Actuators: 31.65 lbf/in^2
Moment Experienced: 5.63 lb*in
Stroke Length: 6 in @ 12⁰
Vertical Force: 15 lbf

## Slide 14: L.V.L.S. Local Vertical Leveling System
James Evans
Optical Feedback Electronic Actuators
Prototype Base
System Logic/Electronics
Actuator Joint

## Slide 15: Prototype Base
James Evans
Landing Gear Concepts designed by Spacecraft Design Team
Support up to 40lbs
Provide stable platform for equipment

## Slide 16: Leveling Component
Four linear actuators placed in an orientation that allows for largest coverage
240 lbs of vertical force
Coupled with optical encoders
Allows for extension and retraction
James Evans

## Slide 17: Actuator Joint
James Evans
Two interlocked hooks prevent dislocation
Spring to create resistance to counter slight tipping on the top platform
Clevis pin connects actuator to joint

## Slide 18: System Logic
Using Arduino Mega 2560
  Communicates orientation data via IMU
  Iterative adjustments comparing current angle to pre-adjust angle
  Coarse adjustment until within ±5° of level, fine adjustment until ±2°
  Optical encoders ensure each actuator moves correct amount
Parker Stensrud

## Slide 19: Leveling Process
Actuators rise 3 inches to its midpoint
IMU takes initial orientation readings
Angle is converted into a linear displacement for the actuators
Opposing actuators will move simultaneously
One axis will level at a time
Parker Stensrud

## Slide 20: Power Distribution
Mean Well SE-450-12 Power Supply
  Outputs 12V at 37.5A
  Fused at 30A
  4 IBT-2 motor drivers wired in parallel
Parker Stensrud

## Slide 21: Hardware
IBT-2 Motor Drivers
  Requires 5V for logic, 12V for motor power
  Allows for independent motor control
  Maximum output of 43A
Parker Stensrud

## Slide 22: Hardware
MPU-6050 IMU
  Requires 5V input
  Communicates via I2C
  Predefined orientation
  Multiple output formats allows for different logic.
Parker Stensrud

## Slide 23: Wiring Schematic
Parker Stensrud
Arduino Mega 2560
Linear Actuator with Optical Encoder
MPU-6050 IMU
IBT-2 43A Motor Driver
12V 37.5A Power Supply

## Slide 24: Testing
Dalton LeClair

## Slide 25: Testing: Test Objectives
Dalton LeClair
System must successfully run between tests without intervention
Mission failure: Actuators must be manually adjusted
Mission success: Actuators automatically return to starting position

## Slide 26: Testing: Test Objectives
Dalton LeClair
Total system leveling must be complete under time constraint
Mission failure > 10 minutes
Mission success < 10 minutes

## Slide 27: Testing: Test Objectives
Dalton LeClair
Must successfully level in any orientation
Mission failure > 5 deg
Mission satisfactory < 5 deg
Mission success < 3 deg

## Slide 28: Testing: Methods
Dalton LeClair
53 in x 53 in platform
Test any orientation
Use 0.87-inch-thick boards to increment 1 degree

## Slide 29: Testing
Dalton LeClair

## Slide 30: Preparing For Space
Stephen Brown
Linear Actuators
Actuator Joint
Electronics

## Slide 31
301 Annealed Stainless Steel
2295 Aluminum Alloy
30 inch Stroke length
4000 Ibs Dynamic force
Withstand 4040 lbf of impact force
Capabilities
Stephen Brown

## Slide 32
3,000 lbs/inch Spring Rate
Inside diameter of 2 inches
316 Stainless Steel Spring
301 Stainless Steel
Spring Specs
Stephen Brown

## Slide 33
4 outputs
Benefits
Centralized Power Distribution
Reduce excess hardware and wires
Save valuable space
Faster response time
Stephen Brown

## Slide 34: Future Work
Assemble and test prototype
Analyze test results
  Make adjustments to optimize design
Explore integrating system into legs
Test until prototype failure
Stephen Brown

## Slide 35: Lessons Learned
Don’t be afraid to question a design if you believe there is a better approach
Communication is essential to working in a team
Using a systems engineering approach ensures all necessary work is accomplished
Mistakes will be made, respond with determination
Stephen Brown

## Slide 36: NASA Self-Leveling System
Team 516:
Stephen Brown
James Evans
Dalton LeClair
Jake Seaman
Parker Stensrud
EML 4551
Connect with us!

## Slide 37: Reference
Admin. (2017, July 27). A guide to aluminum use in the aerospace industry. Retrieved March 19, 2021, from https://continentalsteel.com/blog/aerospace-aluminum-guide/
Premium linear actuators. (n.d.). Retrieved February 13, 2021, from https://www.firgelliauto.com/products/premium-linear-actuators
Reichelt elektronik GmbH & Co. KG Internet Team (webmaster@reichelt.de). (n.d.). ARDUINO MEGA - Arduino Mega 2560, ATmega1280, USB. Retrieved January 11, 2021, from https://www.reichelt.com/de/en/arduino-mega-2560-atmega1280-usb-arduino-mega-p119696.html?GROUPID=6667&&r=1
S. (n.d.). Landing Gear Concepts & Metrics Review. NASA PowerPoint.
Fuchs, Y. (2007, June 28). Lunar Lander Landing System Dynamics Analysis, Testing, and Certification. NASA PowerPoint.
Project apollo diagrams. (n.d.). Retrieved February 13, 2021, from https://history.nasa.gov/diagrams/apollo.html
NASA’s Lunar Exploration Program Overview. (2020, September). Retrieved January 10, 2021, from https://www.nasa.gov/sites/default/files/atoms/files/artemis_plan-20200921.pdf

## Slide 38: Budget
Parker Stensrud

## Slide 39: Prototype Scaling
James Evans
Full Size Lander | 
Dimensions/footprint | 31 ft x 20 ft
Weight | 14-16 tons
Time to level | 1 hour
Scaled Prototype | 
Dimensions/footprint | 50 in x 31 in
Weight | 60 lbs
Time to level | 10 minutes

## Slide 40: Team Introductions
Stephen Brown
Materials Engineer
James Evans
Design Engineer
Dalton LeClair
Test
Engineer
Parker Stensrud
Controls Engineer
James Evans
Jake Seaman
Systems Engineer

## Slide 41: Concept Revision
Worm gear driven linear actuator
Linear actuators will be recessed into the lander base to minimize the distance between legs and capsule.
Benefits of this decision
Dalton LeClair

## Slide 42: Schedule
Parker Stensrud
Not Started
In Progress
Complete
Current Stage

## Slide 43: Prototype Critical Numbers
Impact Force: 129.55 N
Stress on Actuators: 21.82 N/cm^2
Moment Experienced: 63.58 N*cm
Stroke Length: 6 in @ 12⁰
Vertical Force: 66.75 N
James Evans

## Slide 44: Bottle Jack Prototype
Dalton LeClair
Flaws
Many possible failure points
Too much distance between the leg base and the lander cabin
  Potential for tipping

## Slide 45: Future Work
Dalton LeClair

## Slide 46: Schedule
Jake Seaman
In Progress
Not Started
Identified Risk
Current Stage

## Slide 47: Concept Validation
James Evans

## Slide 48: Concept Critical Numbers
Impact Force: 17.97 kN
Stress on Actuators (θ = 12⁰): 31.4 kN/m^2
Moment Experienced: 52.9 kN*m
Stroke Length: 0.762 m @ 12⁰
Vertical Force: 25.2 kN
James Evans

## Slide 50: Wiring Schematic
Controlled by Arduino Mega 2560
  4 L298 Motor Drivers
  4 NEMA17 Steppers
  GY-521 IMU for input
  12V 35Ah battery in parallel used to power the steppers
Dalton LeClair

## Slide 51: Environmental Challenges
Sand-blasting due to regolith
Coefficient of thermal expansion
Cold Welding
Radiation
Dalton LeClair

## Slide 52: Binary Pairwise Comparison
Parker Stensrud
Notes: customer requirements on both axis.

## Slide 53: Binary Pairwise Comparison
Parker Stensrud
Notes: These are customer requirements . Used to get importance weight factor

## Slide 54
Background/scope
Goals
Original design
Secondary design with bottle jacks
Explain challenges/reasons for changing
Introduce new idea&cad and explain individual parts like DR4
Small things we're thinking of improving: bubble levels, wire pathway thing etc
Schedule & expected challenges
Questions: include our QR codes this time?
Use our acronym L.V.L.S.

## Slide 55: House of Quality
Parker Stensrud

## Slide 56: House of Quality
Parker Stensrud

## Slide 57: House of Quality
Parker Stensrud
Notes: engineering characteristics are derived from the functional decomposition

## Slide 58: House of Quality
Parker Stensrud

## Slide 59
James Evans
Bottle Jack
Telescopic legs
Spring System
Gas System
Secondary landing gear
Rack and pinion
Concepts
Datum(slider)
Tripod

## Slide 60
James Evans
Datum(Tripod)
Rack and pinion
Concepts
Bottle Jack
Spring System
Gas System

## Slide 61: Final Three Concepts
James Evans
Bottle Jack
Spring System
Gas System

## Slide 62: Analytical Hierarchy Process
19
James Evans

## Slide 63
Dalton LeClair
Leveling Functions
Sense
Power
Lander
Motion

## Slide 64: Concept Generation
Dalton LeClair
Notes: Remember to say that all the concepts get information from the onboard IMU during the presentation

## Slide 65: Medium Fidelity
Three-Legged Tripod
  Whole leg design
  Integrated into the landing gear
Dalton LeClair
Slider System
XY translation of the lander cabin to move the center of mass until level
Second Landing Gear
Compact until deployed
Multiple arms to lift the lander until level
Gas Release
Piston Cylinder Assembly
Compressed gas in cylinder is released to level
Rack and Pinion
Allow to move upward and downward
Can be fine-tuned

## Slide 66: High Fidelity
Telescopic Legs
  Secondary legs not used for landing
  Four (4) housings containing retracted legs and motor to extend them
  Housing will have brush like bottom to dust off legs upon retraction
Parker Stensrud

## Slide 67: High Fidelity
Spring System
  Begin fully extended
  Springs will be tightened via motors and lowered until level (operates like 3D printer bed)
  Mechanism will be isolated from the elements
Parker Stensrud

## Slide 68
Future Work
January Daily Chart
Summary: The quick brown fox jumps over the lazy dog. The quick brown fox jumps over the lazy dog. The quick brown fox jumps over the lazy dog. The quick brown fox jumps over the lazy dog. The quick brown fox jumps over the lazy dog.
Complete
Identified Risk
In Progress
Not Started
X Days


Milestone 1
Milestone 2

## Slide 69: Team Introductions
Stephen Brown
Materials Engineer
James Evans
Design Engineer
Dalton LeClair
Test
Engineer
Jake Seaman
Systems Engineer
Parker Stensrud
Controls Engineer
James Evans