## Slide 1: ESD- Vision Impaired Technology
Team 522

## Slide 2
Ethan Saffer
David Alicea
Field/Test Engineer and Quality Control
Daa16@my.fsu.edu
Nicolas Garcia
Design Engineer, Webmaster, and Resource Manager
Ng16m@my.fsu.edu
Ethan Saffer
Systems and Design
Engineer
Ers16c@my.fsu.edu
Team 522: Vision Impaired Technology
Madison Jaffe​
Project Manager and Manufacturing/Controls Engineer
Msj16d@my.fsu.edu

## Slide 3: Advisors
Michael Devine
Florida State University
Jim Moran College of Entrepreneurship
Jerris Hooker
FAMU-FSU College of Engineering
Department of Electrical Engineering
Ethan Saffer
Shayne McConomy​
FAMU-FSU College of Engineering​
Department of Mechanical Engineering​

## Slide 4: Introduction
Ethan Saffer
PROBLEM:
The visually impaired have limited aid in current society.
This leaves many of them dependent on others and unemployed.
Median income is $38,500.
Technological aid is often not affordable or effective for their average income.
OUR SOLUTION: HAPTAC
Attaches to the standard white cane.
Senses and scans objects directly ahead.
Alerts users of possible hazards.
Ergonomic handle to remain comfortable for prolonged uses.
Low market price to maximize accessibility.
https://www.semanticscholar.org/paper/An-Implementation-of-an-Intelligent-Assistance-for-Chen-Su/172177515d0b1ee7bcef49cbefecf559c661324f

## Slide 5: Interpreted Customer Needs
Ethan Saffer
1. Helps Avoid Ground Irregularities
2. Allows for Location Awareness
3. Recognizes Surrounding Objects
4. Notify Emergency Contacts
5. Intuitive with O & M Training
6. Identifies and Reads Text
7. Priced for Low-Income Households
whose

## Slide 6: Targets and Metrics
Ethan Saffer
Store Frequent Tasks
Interface with Pre-Existing Skills
Alert of Elevation
Determine Location
Inform User of Possible Threats
Alert of Physical Object
Interpret Sensory Information
Access Emergency Contact
1 GB Worth Of "Tasks"
70% Approval Based on User Feedback
Detect Changes Between 0.6 to 30 cm
±5 m Accuracy in Position
Detect Changes As Fast As 25 m/s
Detect Object From 165 cm Away
Scan and Interpret in ~ 7 Seconds
Contact in 15 Seconds
Importance

## Slide 7: Concept Generation
Detecting Changes Of Elevation
Determine User Location
Detection of Ranged Object
Response to Object Detection
White Cane
Interpret Sensory Information
Infrared Sensor
Ultrasonic Sensor
Ultrasonic Sensor
Lidar
Relative Velocities
Heat
Vibrate
Sound
Poke
Camera
Text To Speech
Imaging To PDF
Text To Braille
GPS Using Internet
GPS With Offline Mapping
Camera Analysis Of Street Signs
Recording Of Previous Trips
Ethan Saffer

## Slide 8
Functions
Ethan Saffer

## Slide 9
The ultrasonic sensors will sense an object up to 3 meters away.
Sense
Functions
Ethan Saffer

## Slide 10
The Raspberry Pi will interpret the sensed information to calculate the proximity to an object.
The ultrasonic sensors will sense an object up to 3 meters away.
Sense
Determine
Functions
Ethan Saffer

## Slide 11
The Raspberry Pi will interpret the sensed information to calculate the proximity to an object.
The ultrasonic sensors will sense an object up to 3 meters away.
Haptic feedback will alert the user with multiple motors with intensity based on distance.
Sense
Determine
Alert
Functions
Ethan Saffer

## Slide 12
The Raspberry Pi will interpret the sensed information to calculate the proximity to an object.
The camera can be activated to scan the desired products.
The ultrasonic sensors will sense an object up to 3 meters away.
Haptic feedback will alert the user with multiple motors with intensity based on distance.
Sense
Determine
Alert
Scan
Functions
Ethan Saffer

## Slide 13
The Raspberry Pi will interpret the sensed information to calculate the proximity to an object.
The camera can be activated to scan the desired products.
The ultrasonic sensors will sense an object up to 3 meters away.
Up to 100 stored products will be in the memory of the Raspberry Pi to identify the product.
Haptic feedback will alert the user with multiple motors with intensity based on distance.
Sense
Determine
Alert
Scan
Identify
Functions
Ethan Saffer

## Slide 14
The Raspberry Pi will interpret the sensed information to calculate the proximity to an object.
The camera can be activated to scan the desired products.
The ultrasonic sensors will sense an object up to 3 meters away.
Up to 100 stored products will be in the memory of the Raspberry Pi to identify the product.
Haptic feedback will alert the user with multiple motors with intensity based on distance.
Haptic feedback will
notify the user when the product has been identified and a speaker will relay the product name.
Sense
Determine
Alert
Scan
Identify
Notify
Functions
Ethan Saffer

## Slide 15
45°
45°* 45°*
Side View:
Top View:
Nicolas Garcia
1 meter
Current Situation
*Based on Standard Technique

## Slide 16
45°
Side View:
Top View:
Nicolas Garcia
5°
3.5 meter
1 meter
15° 15°
45°* 45°*
*Based on Standard Technique
Situation Using HapTac

## Slide 17
Housing
Battery Pack
GrovePi+
Raspberry Pi 4
Vibration Motors (3)
Camera
Ultrasonic Sensor
Nicolas Garcia
Assembly: First Edition

## Slide 18
Scan
The camera can be activated to scan the desired products.
Sense
The ultrasonic sensor will sense an object up to 3 meters away.
Determine
The Raspberry Pi will interpret the sensed information to calculate the proximity to an object.
Notify
Alert
Haptic feedback will alert the user with multiple motors with intensity based on distance.
Identify
Scan
The camera can be activated to scan the desired products.
Sense
The ultrasonic sensor will sense an object up to 3 meters away.
Determine
The Raspberry Pi will interpret the sensed information to calculate the proximity to an object.
Notify
Alert
Haptic feedback will alert the user with multiple motors with intensity based on distance.
Identify
Sense
Sense
Nicolas Garcia
Assembly: First Edition
Thin walls and sharp tip led to stress concentration

## Slide 19
Nicolas Garcia
Assembly: Second Edition

## Slide 20
The handle is too wide, the user's fingers are not able to completely wrap around it.
The groove for the thumb is placed higher than what is comfortable
Nicolas Garcia
Assembly Concerns: Handle

## Slide 21
Nicolas Garcia
Made shorter.
Slimmer profile.
Flat bottom for efficient printing.
Opening for button at thumb groove
  Enables camera use.
Assembly Concerns: Addressed

## Slide 22
Madison Jaffe
Too much excess room.
The ultrasonic sensors cannot be properly mounted.
Did not include spots to mount all components.
*Battery and speaker not pictured
Assembly Concerns – Main Housing

## Slide 23: Assembly: Third Edition
Madison Jaffe

## Slide 24: Assembly Concerns: Distribution
Shelf Location
Puts Pressure on Components.
Blocked Speaker.
Cane Attachment
Blocked Camera Wiring.
Mounting
Exterior Walls Are Too Thin.
Holes Are Not Deep/Wide Enough.
Battery
Bend in Cable Is Not Accounted For.
Power Button Is Not Properly Located.
Needs More Rigidity.
Madison Jaffe

## Slide 25: Assembled View: Final Product
Madison Jaffe
36.6 cm
9.95 cm
12 cm

## Slide 26
Lid
Shelf
Main Housing
Handle
Push Button
Button
Wing Screw
Clamp
Battery
Vibration Motors (3)
Camera
Ultrasonic Sensors (3)
Raspberry Pi 4
GrovePi+
Exploded View
Speaker
Madison Jaffe

## Slide 27: Raspberry Pi: Sensors and Motors Code
Motor is turned off
Motor is turned on
and off at 0.5 second intervals
Motor is turned on
David Alicea
Sensors are turned on
Distance <= 100
Yes
100 < Distance <= 200
Yes
No
200 < Distance <= 300
No
Yes
No
Distance > 300
Yes
Object distance measured (cm)
Motor is turned on
and off at 1 second intervals

## Slide 28: Sensor Validation
2.54 cm (1 inch)
30.48 cm (12 Inches)
7.62 cm (3 Inches)
David Alicea

## Slide 29: Sensor Limitations
Ultrasonic sensor is directed forward and does not support large changes in angle or tilt.
O
B
J
E
C
T
O
B
J
E
C
T
David Alicea

## Slide 30: Item Identification on HapTac
David Alicea
Device is turned on
Button is pressed
Camera is activated
Camera takes
a picture of the object
1Image is saved as a file
Alexnet takes image file and begins identifying
Alexnet gives prediction of what the object is
Speaker tells user what the object is
1The same file is used for each use, therefore only the last image taken is saved on the device. Each image is deleted once a new one is taken.

## Slide 31
Why does it only detect the plastic bag?
Database has bias towards the plastic bag.
Nearly no instance of flour bags in database.
When scanned, overall shape is evaluated.
Nicolas Garcia
AlexNet – Normal Conditions

## Slide 32
Nicolas Garcia
AlexNet – Lower Light Conditions

## Slide 33
Nicolas Garcia
AlexNet – Various Objects in Frame
Software will analyze centerline first, even in low light conditions.

## Slide 34: Validation
Function | Target
Alert of Elevation* | 0.6 to 30 cm
Determine Location* | Margin of error of at most 5 meters
Alert of Physical Object* | 165 cm
Identify Possible Threats* | Up to 25 m/s
Access Emergency Contact | 15 seconds
Interpret Sensory Information* | 7 seconds
Store Frequent Tasks | 1 GB
Interface with Pre-Existing Skills | 70%
Compete within Market | 20%
Remain Lightweight | <2.3 kg
Remain Discrete | 70% User Approval
Ethan Saffer
*: Critical Function

## Slide 35: Validation
Function | Target | Complete
Alert of Elevation* | 0.6 to 30 cm | Yes
Determine Location* | Margin of error of at most 5 meters | No
Alert of Physical Object* | 165 cm | Yes
Identify Possible Threats* | Up to 25 m/s | No
Access Emergency Contact | 15 seconds | No
Interpret Sensory Information* | 7 seconds | Yes
Store Frequent Tasks | 1 GB | Yes
Interface with Pre-Existing Skills | 70% | Yes*
Compete within Market | 20% | Yes
Remain Lightweight | <2.3 kg | Yes
Remain Discrete | 70% User Approval | N/A
Ethan Saffer
*: Critical Function

## Slide 36: Validation
Function | Target | Completion Metric
Alert of Elevation* | 0.6 to 30 cm | 0.6 to +30 cm
Determine Location* | Margin of error of at most 5 meters | Needs GPS, we should eliminate it
Alert of Physical Object* | 165 cm | 203 cm detection (high precision)
Identify Possible Threats* | Up to 25 m/s | Interpolation between sensors scans for threats
Access Emergency Contact | 15 seconds | No
Interpret Sensory Information* | 7 seconds | Scans and relays scanned object within 4-6 seconds
Store Frequent Tasks | 1 GB | Yes
Interface with Pre-Existing Skills | 70% | Yes*
Compete within Market | 20% | 67% cheaper than top competitor
Remain Lightweight | <2.3 kg | 1.2 kg (Including cane)
Remain Discrete | 70% User Approval | N/A
Ethan Saffer
*: Critical Function

## Slide 37: Summary
Ideas had to be dismissed due to scope creep.
  May still be integrated in the future.
Cheaper parts for prototype made it cost efficient to market.
  Ultimately affected the accuracy of the device.
Overall, the project is successful in fulfilling its functions despite limitations.
Ethan Saffer

## Slide 38: Reference
Ethan Saffer
[1] Ebben, J. M., PhD. (n.d.). Wrists at risk: Awkward postures to avoid. Retrieved February 18, 2021, from https://www.iacindustries.com/get-started/ergonomics/wrists-at-risk.asp
[2] González, A., Salgado, D., García Moruno, L., & Sánchez Ríos, A. (2018). An Ergonomic Customized-Tool Handle Design for Precision Tools using Additive Manufacturing: A Case Study. Applied Sciences, 8(7), 1200. doi:10.3390/app8071200
[3] McConomy, S. (2020, November 11). Engineering Characteristics, Functions, Targets, and Metric. FAMU-FSU College of Engineering.
[4] National Federation of The Blind. https://www.nfb.org/resources/blindness-statistics
[5] Queen, K. (2016, June). 7 Ways to Make Communities More Livable for People With Vision or Hearing Impairments. AARP.
[6] Rosen, S. (n.d.). LONG CANE TECHNIQUES. Retrieved March 03, 2021, from https://tech.aph.org/sbs/04_sbs_lc_study.html
[7] Wang, C., & Cai, D. (2020). Hand tool handle size and shape determination based on hand measurements using a contour gauge. Human Factors and Ergonomics in Manufacturing &amp; Service Industries, 30(5), 349-364. doi:10.1002/hfm.20846

## Slide 39
Ethan Saffer
David Alicea
Field/Test Engineer and Quality Control
Daa16@my.fsu.edu
Nicolas Garcia
Design Engineer, Webmaster, and Resource Manager
Ng16m@my.fsu.edu
Ethan Saffer
Systems and Design
Engineer
Ers16c@my.fsu.edu
Team 522: Vision Impaired Technology
Madison Jaffe​
Project Manager and Manufacturing/Controls Engineer
Msj16d@my.fsu.edu

## Slide 42
APPENDIX

## Slide 43: Raspberry Pi and Grove Parts
Raspberry Pi acts as our main processing unit.
Grove Pi is the attachment board that makes the Grove parts accessible.
Raspberry Pi Camera is used to identify items.
Ultrasonic sensors and vibration motors detect objects and notify the user of their presence.
David Alicea

## Slide 44: Lessons Learned
The front of the main housing has a downward bend.
Corners are warped, altering geometry
Madison Jaffe
3D Printing is good for quick models
Warping and geometric constraints limit their use

## Slide 45
The battery served as the hardest object to design around.
  It is the largest and heaviest component of our assembly
New iterations of housing were made to make it as compact as possible.
Lessons Learned
Madison Jaffe
May not receive the parts originally desired.
Need to be constantly adapting to changes.

## Slide 46: Lessons Learned
Proper calibration of sensors and motors are pivotal for their accurate usage.
Here the sensor should read 7.6cm, rounded between 7 and 8.
  The error propagates further as the distance increases
David Alicea
7.6 Centimeters
Calibration is essential to precise measurements.
Propagation of error can be reduced.

## Slide 47: InNOLEvation Challenge
Competed in the InNOLEvation Competition
Selected as a finalist
  Received $500 for the company
Ethan Saffer
Unit Price: $299
Yearly Projections

## Slide 48: Third Housing

## Slide 49: Third Housing

## Slide 50: Assembly Concerns: Addressed
Megapascals (MPa)
The orange shows where the stress is highest.
Nicolas Garcia

## Slide 51: Housing Validation
Madison Jaffe

## Slide 52: Housing
Original housing includes:
  1 Ultrasonic sensor
  3 Vibration Motors
  Raspberry Pi / Grove Pi+
  Accelerometer & Gyroscope
  Valve clamp
Ethan Saffer

## Slide 53: Camera Identification - AlexNet
Nicolas Garcia

## Slide 54: Housing Validation
Megapascals (MPa)
The orange shows where the stress is highest.
Madison Jaffe

## Slide 55
Ethan Saffer
Housing

## Slide 56: Key Goals and Assumptions
Key Goals:
  Aids the visually impaired in daily activities.
  Assist people who are visually impaired to become more active.
  Keep the visually impaired safe while executing relatively complex tasks.
Assumptions:
  Users are unaware of objects in new surroundings.
  Users have undergone Orientation and Mobility training/rehabilitation.
  The visually impaired are not fully comfortable in our current society.
Ethan Saffer

## Slide 57: Critical Functions
Alert of Elevation
Determine Location
Alert of Physical Object
Identify Possible Threats
Interpret Sensory Information
Ethan Saffer

## Slide 58: Raspberry Pi: Sensors and Motors Code
David Alicea

## Slide 60: Yearly Projections
Madison Jaffe
3 Year Sales Projection
Projected Revenue
  $594,631
Projected Profit
  $184,543
5 Year Sales Projection
Projected Revenue
  $1,807,101
Projected Profit
  $250,639
35% Growth from Year 3

## Slide 61: Housing
Our previous housing design was failing at the cane attachment.
The new design is more capable of handling the stresses that will act on the housing.
Nicolas Garcia

## Slide 62: Housing Concerns: Warping
The front of the main housing has a downward bend.
Corners are warped, altering geometry

## Slide 63: Medium-High Fidelity Concepts
Ethan Saffer
GPS Watch:
Haptic Feedback cane:
Smart Glasses:
Audio Feedback cane:
GPS app:
Pin Matrix Haptics:
Sensor Watch:
Sensor Pin Chip:

## Slide 64: Markets
Ethan Saffer
  Primary market: People with severe visual impairment, rehabilitation and treatment centers.
  Secondary market: Autonomous Systems and State-Local Departments of Transportation.

## Slide 65: Final Selection
Our final potential designs were ranked:
  Haptic Smart Cane
  Sensor Pin Chip
  Sensor Watch
#2
Sensor Pin Chip
#1
Haptic Smart Cane
#3
Sensor Watch
Ethan Saffer

## Slide 66
White Cane
Sunu Band
WeWalk
https://athome.medline.com/en/medline-white-cane-for-blind-vision-impaired-1ct-mdswhtcane
https://www.sunu.com/es/index
https://webrazzi.com/en/2020/05/01/wewalk-investment-750k/
Ethan Saffer
Competitors

## Slide 67: WeWalk
Similar product that incorporates ultrasonic sensors in the format of a smart-cane.
Uses infrared sensors to detect ground irregularities.
Overload of information.
Ethan Saffer

## Slide 68: Competitor Comparison
White Cane | Sunu Band | WeWalk | Our Solution
Senses irregularities below the waist Standard aid for visually impaired | Senses objects nearby Set position on wrist, can discomfort user to "aim" | Infrared Sensor for floor irregularities Ultrasonic sensor for object detection | Senses ground irregularties Notifies user

## Slide 69: Device Operational Time
Ultrasonic Sensor
8 mA
Camera
Up to 800 mA
Vibration Motor
58 mA average
100 mA max
Raspberry Pi
3,000 mA
Power Supply
20,000 mAh
Theoretical (Maximum Current Draw) Operation Time: 4.87 Hours
4 hours, 52 minutes and 12 seconds
Madison Jaffe

## Slide 70: Targets and Metrics
Function | Target | Metric
Alert of Elevation* | 0.25 to 12 inches | Distance
Determine Location* | ~ 16 feet | Distance
Alert of Physical Object* | 65 inches | Distance
Identify Possible Threats* | Up to 60 miles per hour | Velocity
Access Emergency Contact | 15 seconds | Time
Interpret Sensory Information* | 7 seconds | Time
Store Frequent Tasks | 1 GB | Memory Allocation
Interface with Pre-Existing Skills | 70% | User Satisfaction
Compete within Market | 20% | Price Range USD ($)
Remain Lightweight | < 5.1 lb | Weight
Remain Discrete | 70% | User Approval
David Alicea

## Slide 71: Concept Generation Tools
Biomimicry
Crap Shoot
Morphological Chart
David Alicea
McConomy, S. (2020, November 11). Engineering Characteristics, Functions, Targets, and Metric. FAMU-FSU College of Engineering.

## Slide 72: Medium Fidelity Concepts
David Alicea
GPS Watch:
- GPS indicate where the user is
- haptic feedback provided through vibration on wrist
Haptic Feedback cane:
- haptic feedback voice-activated
- phone compatible
Smart Glasses:
- sensor and GPS for user location
- Audio feedback through glass-mounted earpiece
Audio Feedback cane:
- audio feedback
- Tactile or voice activation
- Phone compatible
- camera to interpret the environment
GPS app:
- Lidar
- user information through haptics
- computer and GPS track and locate user

## Slide 73: Concept Selection
David Alicea

## Slide 74: Pugh Chart
Nicolas Garcia

## Slide 75: Pugh Chart
Nicolas Garcia

## Slide 76: Second Pugh Chart
Nicolas Garcia

## Slide 77: Second Pugh Chart
Nicolas Garcia

## Slide 78: Analytical Hierarchy Process
Nicolas Garcia
Criteria Comparison Matrix [C] | 
Functions | Criteria Weights{W}
Alert of Elevation | 0.11
Determine Location | 0.13
Interpret Sensory Information | 0.24
Access Emergency Contact | 0.03
Interface With Pre-Existing Skills | 0.11
Store Frequent Tasks | 0.04
Alert of Physical Object | 0.19
Inform User of Possible Threats | 0.15
Sum | 1.00

## Slide 79: Analytical Hierarchy Process
Nicolas Garcia
 | Sensor Pin Chip | Sensor Watch | Haptic Smart Cane
Alert of Elevation | 0.11 | 0.11 | 0.78
Determine Location | 0.16 | 0.19 | 0.66
Interpret Sensory Information | 0.45 | 0.45 | 0.09
Access Emergency Contact | 0.20 | 0.20 | 0.60
Interface with Pre-existing Skills | 0.14 | 0.14 | 0.71
Store Frequent Tasks | 0.33 | 0.33 | 0.33
Alert of a Physical Object | 0.43 | 0.14 | 0.43
Inform User of Possible Threats | 0.33 | 0.33 | 0.33

## Slide 80: Analytical Hierarchy Process
Nicolas Garcia
 | Sensor Pin Chip | Sensor Watch | Haptic Smart Cane
Alert of Elevation | 0.11 | 0.11 | 0.78
Determine Location | 0.16 | 0.19 | 0.66
Interpret Sensory Information | 0.45 | 0.45 | 0.09
Access Emergency Contact | 0.20 | 0.20 | 0.60
Interface with Pre-existing Skills | 0.14 | 0.14 | 0.71
Store Frequent Tasks | 0.33 | 0.33 | 0.33
Alert of a Physical Object | 0.43 | 0.14 | 0.43
Inform User of Possible Threats | 0.33 | 0.33 | 0.33

## Slide 81: Analytical Hierarchy Process
Nicolas Garcia
 | Sensor Pin Chip | Sensor Watch | Haptic Smart Cane
Alert of Elevation | 0.11 | 0.11 | 0.78
Determine Location | 0.16 | 0.19 | 0.66
Interpret Sensory Information | 0.45 | 0.45 | 0.09
Access Emergency Contact | 0.20 | 0.20 | 0.60
Interface with Pre-existing Skills | 0.14 | 0.14 | 0.71
Store Frequent Tasks | 0.33 | 0.33 | 0.33
Alert of a Physical Object | 0.43 | 0.14 | 0.43
Inform User of Possible Threats | 0.33 | 0.33 | 0.33

## Slide 82: Standard Shapes
Summary Box
Text box 1
Outlined Text Box

## Slide 83: Approved Logos

## Slide 84: Color Palette

## Slide 85
Slides to keep:
Intro, Synopsis of VDR1 (Rename), Customer Needs, minimize Concept Gen. & Selection, Final Selection?, What's Next, Last team member slide, Ref.
Slides to add:
Specs of design
BOM/Ordering parts
Our progress in the InNOLEvation challenge?

## Slide 86: APA Tables
Category 1 | Category 2 | Category 3 | Category 4 | Category 5
Item 1 |  |  |  | 
Item 2 |  |  |  | 
Item 3 |  |  |  | 
Item 4 |  |  |  | 
 | Category 2 |  |  | Category 3 | 
Category 1 | subcategory 1 | subcategory 2 |  | subcategory 1 | subcategory 2
Item 1 |  |  |  |  | 
Item 2 |  |  |  |  | 
Item 3 |  |  |  |  | 
Item 4 |  |  |  |  |