## Slide 1
ENVIRONMENTALLY CONTROLLED TEST CHAMBER
TEAM 503
Nicholas Blenker | Tucker Hall | David Wilson

## Slide 2
Meet Team 503
Design Engineer
Systems Engineer
Controls Engineer
David Wilson
Nicholas Blenker
Tucker Hall
Tucker Hall

## Slide 3
Sponsor & Advisor
Danfoss
FAMU-FSU College of Engineering
William Bilbow
Keith Larson

## Slide 4
Original Design
DUCTWORK
CONTROL
VOLUME
AIR HANDLING
UNIT
CHAMBER
COMPRESSOR
TREATED AIR
RETURN AIR

## Slide 5
Floor-Mounted AHU​
Detachable Side Ducts​
29,000 BTU A/C​
Industrial Humidifier
3
4
2
1
Key Changes
New Design

## Slide 6
1
Floor-Mounted AHU
Very limited wall space available
Suggested by lab staff
Significantly reduced length of ductwork
  Decreases heat transfer with surroundings
Increased mobility/portability
Reasoning

## Slide 7
Detachable Side Ducts
Ductwork easily removable
Side ducts are more accessible
Significantly reduced length of ductwork
  Decreases heat transfer with surroundings
Increased mobility/portability
Reasoning
2

## Slide 8
3
29,000 BTU A/C
More versatile
Most value in terms of power versus cost
  Only ~$500 more than 1/2 as powerful
Compensates for leaks, infiltration, and other possible issues
Decreases time to desired conditions
Comes with built-in ductwork
Reasoning
3

## Slide 9
Industrial Humidifier
Ensures that 95% RH can be reached
Comes with large tank
  Doesn't need to be refilled often
Ensures that any condition can be met within 15 minutes
Features built-in automated control system
4
Reasoning

## Slide 10: Air Cooled Portable AC
Vendor: NorthStock
Quantity: 1
Features:
  29,000 BTU, 230V/1P/60Hz
  0-30 C spot cooling
  Ambient air: 45 C max
Cost: $3,456.99
Link: Click Here
10

## Slide 11: Industrial Humidifier
11
Vendor: Amazon
Quantity: 1
Features:
  45-95% RH, 24L Tank
  110V
  Intelligent control system
Cost: $289.98
Link: Click Here

## Slide 12: Electric Strip Heaters
12
Vendor: McMaster-Carr
Quantity: 2/3
Features:
  500W, no controller
  120V/1P
  8" x 1.5" x 0.3125"
Cost: $42.86 ea ($126.58)
Link: Click Here

## Slide 13: Fiberglass Duct Insulation
13
Vendor: Grainger
Quantity: 1
Features:
  0.75 lb density
  48" wide, 25' long
  R-value: 4.2
Cost: $67.54
Link: Click Here

## Slide 14: Duct Sealant
14
Vendor: Lowe's
Quantity: 1
Features:
  Fiber reinforced, water-based, high velocity
  Joints, seams, penetrations
Cost: $16.58
Link: Click Here

## Slide 15: Duct Take-Off
15
Vendor: Lowe's
Quantity: 3
Features:
  Fits 6" duct
  Galvanized steel
  Airtight adhesive gasket
Cost: $8.98 ea ($26.94)
Link: Click Here

## Slide 16: Clear Vinyl
16
Vendor: MarineVinylFabric
Quantity: 3 (yards)
Features:
  54" wide, 80 gauge/2 mm
  Marine grade, durable, flexible
Cost: $26.95 ea ($80.85)
Link: Click Here

## Slide 17: Temperature & Humidity Sensor
17
Vendor: TTI
Quantity: 4
Features:
  +/- 0.3 C
  -40 C ≤ T ≤ 125 C
  +/- 3% RH (0-100%)
Cost: $8.02 ea ($32.08)
Link: Click Here

## Slide 18: Humidity Sensor
18
Vendor: TTI
Quantity: 4
Features:
  Analog output
  +/- 1% error
  1% to 99% RH
Cost: $5.39 ea ($21.56)
Link: Click Here

## Slide 19: T-shaped Rubber Sealing Strips
19
Vendor: AliExpress
Quantity: 1
Features:
  Sound insulation
  Waterproof
  Dustproof sealing strip
Cost: $30.75
Link: Click Here

## Slide 20: Foam Sealing Strip
20
Vendor: Amazon
Quantity: 2
Features:
  1" x 0.75" x 13'
  Waterproof, high density
  Single-sided adhesive
Cost: $20.79 ea ($41.58)
Link: Click Here

## Slide 21: Arduino Mega
21
Vendor: Amazon
Quantity: 1
Features:
  USB connector
  Arduino IDE compatible
  5V operating voltage
Cost: $17.49
Link: Click Here

## Slide 22: Breadboard Jumper Wires
22
Vendor: Amazon
Quantity: 1
Features:
  Insulation Material: PVC
  Conductor material: Copper tinned
  Of multiple variety
Cost: $17.99
Link: Click Here

## Slide 23: Unfinalized Items
Condensate pump*
Vendor: Koldwave
Quantity: 1
Features:
  Removes existing condensation from the system
  Makes the system more efficient
Cost: $439.45
Link: Click Here
* Not sure if necessary
* Can select other cheaper options
23
Ambient air adapter
Vendor: Koldwave
Quanity: 1
Features:
  Fits over the intake air vent
  Would attach to the chamber via ductwork, creating a closed-loop system
  Eliminates the issue of pressurization
Cost: Unknown (awaiting response)

## Slide 24
24
Summary
Biggest Spenders:
AC Unit: $3,457
Humidifier: $290
Strip Heaters: $126
Total does not account for the two unfinalized items
Total Cost $ 4,842.01
Approximated Budget $ 5,000.00
= Cost Ratio 97%

## Slide 25: Meeting Notes
Risk Factors
  Condensation
    Fires
    Electric shock
  Heating Strips
    Fire
    Temperature accuracy
Mobilize System
  Simple plywood stand with wheels
  Reduces electrical risk
Perform Hazard Assessment
Complete FMEA