## Slide 1
¼” eye bolt (4x)
3D Printed base
Arduino Mega
3D Printed Lexan frame
Lexan window
Stepper motor
3D Printed ArduCam Mini housing
AIAA: NASA Student Launch Competition
Team 501 | Jedreck Acquissa | Peyton Breland | Dylan Gardner | Mark Ioffredo | Zachary Isriel
Sponsors: Shayne McConomy, Ph.D. & William Oates, Ph.D. | Advisor: Chiang Shih, Ph.D.
Fly a high-powered solid motor rocket to an altitude of 4,600 ft that will deploy a payload. The payload must be capable of receiving and executing a string of radio frequency (RF) commands once it reaches the ground with the launch vehicle. The launch competition will be on April 15, 2023, in Huntsville, AL.
Objective
Targets
Payload
Modeling, Simulations, & Flight Tests
A combination of OpenRocket, SolidWorks, and PTC Creo were used to design and simulate the flight vehicle. OpenRocket simulations were performed to study the vehicle’s performance under various wind speeds and internal loads. CFD and FEA performed on multiple vehicle components to ensure its integrity and robustness
The payload is a stationary device deployed from the upper payload bay along with the main parachute upon descent. Once the vehicle has landed, the payload will receive a RF sequence of string commands from NASA and decode it to capture images at certain angles then process them to generate different filters.
LD – Haack Series Nose Cone
Upper PB
Lower PB
Avionics Bay
Motor & Fin Can
Landing Impact Energy
< 75 ft-lb
Wind Drift Distance
< 2500 ft
Thrust-to-Weight Ratio
> 5:1
Stability Margin
2-5 calibers
Total Descent Time
< 85 s
Altitude
4600 ± 100 ft