## Slide 1: Hybrid Vehicle Battery Cooling
Team 507: Anthony Vicary | Chris Carley | Clayton Carlson | Corey Kelley | Jacob Owens

## Slide 2: TEAM 507
Chris Carley
Manufacturing Engineer
Corey Kelley
Systems
Engineer
Clayton Carlson
Thermal Fluid Engineer
Anthony Vicary
Heat Transfer
Engineer
Jacob Owens
Design Engineer

## Slide 3: Sponsor and Advisor
Dr. Michael Hayes
Cummins, Inc
Material Engineer
Dr. Juan Ordonez
FAMU-FSU College of Engineering

## Slide 4: Project Objective
The objective of this project is to design a cooling method for a hybrid vehicle battery pack that is at least 5% more effective than current industry standards.

## Slide 5: Background
Lead to development of hybrid and electric trucks
Increased emissions standards and improvements in Lithium-Ion Batteries

## Slide 6: Background
Exposure to high temperatures degrades Lithium-Ion Batteries
Exposure to low temperatures increases internal resistance within battery

## Slide 7: Background
Acceleration requires large amounts of power
Large current is produced within the battery and large amount of heat are produced
Cooling methods must keep up with increase thermal loads

## Slide 8: Battery Pack Components
Battery Pack
Module
Pouch Cell

## Slide 9
Key Goals
Improve battery cooling effectiveness
Design focuses on innovation at module level
Keep cost of ownership down
Keep battery within efficient operating temperature

## Slide 10: Assumptions
Design will be based on a Nissan Leaf pouch cell module
Domain of project will be within battery enclosure
Battery will be subjected to a variety of operating conditions
Not able to physically open a battery module
Notes: Mention that design will be implemented with 10 kWh battery pack in mind but will be scalable for larger battery packs

## Slide 11: Customer Needs
Concept must be lightweight
Works at extreme temperatures
Handle high heat transfer rates
Prevents puncture to pouch cells
Keep pumping power to a minimum
Implement at module level

## Slide 12: Functions
Battery Cooling Method
Heat Transfer
Safety
Efficiency
Chris Carley

## Slide 13: Heat Transfer: Functions
Heat Transfer
Cools Battery
Chris Carley

## Slide 14: Safety: Functions
Safety
Avoids Puncture
Reduces Thermal Runaway
Withstands Thermal Cycling
Accommodate Swelling
Chris Carley

## Slide 15: Efficiency: Functions
Efficiency
Minimize Weight
Minimize Energy Loss
Chris Carley

## Slide 16: Critical Targets
Temperature
Under 40° Celsius
Size
261x216x8mm
Puncture
110 MPa

## Slide 17: Critical Targets
Long Lasting
10 years
Weight
20% module weight
Pressure Loss
1 kPa

## Slide 18: Initial Design: Cooling Pipes around Inner wall of Module
Coolant Channel
Coolant inlet and outlet
Coolant channels fit within module walls

## Slide 19
Initial Design
Revised Design

## Slide 20: Pressure Loss
Universiteit Brussel Research
Initial Coolant Channel
Flow Rate: 0.2 m/s
Channel Length: 1 m
Pressure loss: 475 pa
Revised Coolant Channel
Flow Rate: 0.2 m/s
Channel Length: 0.75 m
Pressure loss: 350 pa

## Slide 21: Module Assembly

## Slide 22: Physical Prototype
Top Plate
Bottom Plate

## Slide 23: Physical Prototype
Inlet Connector
Outlet Connector
Thermocouple Connection
RTV Gasket Glue

## Slide 24: COMSOL
The new CAD model has been imported into COMSOL for thermal analysis.
Currently developing a simulation of the full module.
293 K
300 K

## Slide 25: Materials Selection
12V 2 GPM PowerFLO Diaphragm Pump
½" Thick 12" x 12" Aluminum Plate
MAX6675 K-Type Thermocouple
Gasket Glue

## Slide 26: Materials Selection
Nylon Hose
3D Printer Silicone Heated Pad 120V 150W
3/8” OD Push to Connect Fittings

## Slide 27: Testing Plan
Dry Test
Steady Test
Transient Test
Coolant will flow once heating pads reach steady temperature.
Coolant will flow while heating pads are still gaining temperature.
Results will serve as benchmark to base cooling method effectiveness.
Parameter Matching
Temperature, mass flow rate, and pressure loss will be found experimentally and be compared to simulation results.

## Slide 28: Testing Plan
Aluminum
Wood
Aluminum
Wood
Module Housing Material

## Slide 29: Budget
Chart: T507 Total Budget
| Total Spent | Total Unspent
 | 822.06 | 1177.94
Chart: T507 Budget Breakdown
| Raw Materials | Hardware | Tubing & Connections | Test Materials
 | 228.18 | 254.01 | 127.06 | 212.79

## Slide 30: Future Work
Manufacture Physical Model
Assemble Testing Setup
Finish COMSOL Simulations

## Slide 31
Thanks for listening
Anthony Vicary | Chris Carley | Clayton Carlson | Corey Kelley | Jacob Owens
Anthony Vicary
Chris Carley
Corey Kelley
Jacob Owens
Clayton Carlson

## Slide 32: References
Goutam, S., Nikolian, A., Jaguemont, J., Smekens, J., Omar, N., Van Dan Bossche, P., & Van Mierlo, J. (2017). Three-dimensional electro-thermal model of li-ion pouch cell: Analysis and comparison of cell design factors and model assumptions. Applied Thermal Engineering, 126, 796–808. https://doi.org/10.1016/j.applthermaleng.2017.07.206

## Slide 34: Backup Slides

## Slide 35: Physical Prototype

## Slide 36: Physical Prototype

## Slide 37: Budget Breakdown Sheet
Raw Materials | Hardware | Tubing & Connections | Test Materials
$228.18 | $254.01 | $127.06 | $212.79

## Slide 38: Total Spent Sheet
Total Spent | Total Unspent
$822.06 | $1,177.94

## Slide 39: Raw Materials Table
Raw Materials |  |  |  |  | 
Item | Part Description | Quantity | Unit Cost | Total Cost | Category Cost
1 | Aluminum Plate 6061: T6511, 12 in Overall Lg, 10 in Overall Wd, 0.5 in Thick, Mill, +/-0.009 in, B95 | 2 | $50.49 | $100.98 | $228.18
2 | Aluminum Plate 6061: T6511, 12 in Overall Lg, 12 in Overall Wd, 0.5 in Thick, Mill, +/-0.009 in, B95 | 2 | $63.60 | $127.20 | 

## Slide 40: Hardware Table
Hardware |  |  |  |  | 
Item | Part Description | Quantity | Unit Cost | Total Cost | Category Cost
1 | 2Pcs Silicone Car Engine Heater Pad - 4" x 5" Self-Adhesive Oil Pan Heater Pad with 194°F Thermal Protector, 120V 150W Car Battery Warmer Pad Engine Block Heater Pad with 68" Long Power Cord (Orange) | 2 | $20.99 | $41.98 | $254.01
2 | BCZAMD 120V 500W Silicone Heating Pad 235 X 235mm Rubber Heater Mat with NTC 100K Thermistor Strong Adhesive for Crealit Ender 3 V2 3S Ender 5 3D Printer Heated Bed | 3 | $35.99 | $107.97 | 
3 | 12V 2 GPM PowerFLO Automatic Demand Diaphragm Pump | 1 | $87.07 | $87.07 | 
4 | 4 Sets DC 3-5V MAX6675 Thermocouple Module and K Type Thermocouple Temperature Sensor Thermocouple Sensor Set M6 Screw with Cable Cord Compatible with Arduino Raspberry Pi | 1 | $16.99 | $16.99 | 

## Slide 41: Tubing & Connections Table
Tubing & Connections |  |  |  |  | 
Item | Part Description | Quantity | Unit Cost | Total Cost | Order Cost
1 | 25 ft long Nylon Hose | 1 | $58.29 | $58.29 | $127.06
2 | Brass Barbed Hose Fitting for Air and Water Straight Adapter for 5/16" Hose ID, 3/8 NPTF Male | 1 | $18.95 | $18.95 | 
3 | Push-to-Connect Tube Fitting with Universal Thread for Air and Water, Adapter, 3/8" Tube OD x 1/4 Pipe | 6 | $3.65 | $21.90 | 
4 | Shark Industrial Premium Stainless Steel Dishwasher Hose - 10 FT No-Lead Burst Proof Water Supply Line 3/8" comp x 3/8" comp with attached 90 degree 3/8" comp x 3/8" MIP elbow - 10 year warranty | 1 | $12.95 | $12.95 | 
5 | 1/4 in. - 3/8 in. Tubing Bender | 1 | $14.97 | $14.97 | 

## Slide 42: Testing Materials Table
Test Materials |  |  |  |  | 
Item | Part Description | Quantity | Unit Cost | Total Cost | Order Cost
1 | Ultra Black® Oil Resistant RTV Silicone Gasket Maker, 3.35 Tube | 2 | $14.38 | $28.76 | $212.79
2 | Prestone DEX-COOL Antifreeze+Coolant; Extended Life -1 Gal- Ready to Use, 50/50 | 2.00 | $22.20 | $44.40 | 
3 | Great Value Aluminum Foil, 225 sq ft | 9 | $10.63 | $95.67 | 
4 | Rubbermaid Commercial Products 2.5 Gallon Brute Heavy-Duty, Corrosive-Resistant, Round Bucket, Red FG296300RED | 2 | $21.98 | $43.96 |