## Slide 1: Hybrid Vehicle Battery Cooling
Team 507: Anthony Vicary | Chris Carley | Clayton Carlson | Corey Kelley | Jacob Owens

## Slide 2: TEAM 507
Chris Carley
Manufacturing Engineer
Corey Kelley
Systems
Engineer
Clayton Carlson
Thermal Fluid Engineer
Anthony Vicary
Heat Transfer
Engineer
Jacob Owens
Design Engineer

## Slide 3: Sponsor and Advisor
Dr. Michael Hayes
Cummins, Inc
Material Engineer
Dr. Juan Ordonez
FAMU-FSU College of Engineering

## Slide 4: Project Objective
The objective of this project is to design a cooling method for a hybrid vehicle battery pack that is at least 5% more effective than current industry standards.

## Slide 5: Background
Lead to development of hybrid and electric trucks
Increased emissions standards and improvements in Lithium-Ion Batteries

## Slide 6: Background
Exposure to high temperatures degrades Lithium-Ion Batteries
Exposure to low temperatures increases internal resistance within battery

## Slide 7: Background
Acceleration requires large amounts of power
Large current is produced within the battery and large amount of heat are produced
Cooling methods must keep up with thermal loads

## Slide 8: Battery Pack Components
Battery Pack
Module
Pouch Cell

## Slide 9
Key Goals
Improve battery cooling effectiveness
Design focuses on innovation at module level
Keep cost of ownership down
Keep battery within efficient operating temperature

## Slide 10: Assumptions
Design will be based on a Nissan Leaf pouch cell module
Domain of project will be within battery enclosure
Battery will be subjected to a variety of operating conditions
Not able to physically open a battery module
Notes: Mention that design will be implemented with 10 kWh battery pack in mind but will be scalable for larger battery packs

## Slide 11: Customer Needs
Concept must be lightweight
Works at extreme temperatures
Handle high heat transfer rates
Prevents puncture to pouch cells
Keep pumping power to a minimum
Implement at module level

## Slide 12: Functions
Battery Cooling Method
Cool Battery
Safety
Efficiency
Corey Kelley

## Slide 13: Heat Transfer: Functions
Cool Battery
Transfer Heat
Corey Kelley

## Slide 14: Safety: Functions
Safety
Avoids Puncture
Reduces Thermal Runaway
Withstands Thermal Cycling
Accommodate Swelling
Corey Kelley

## Slide 15: Efficiency: Functions
Efficiency
Minimize Weight
Minimize Energy Loss
Corey Kelley

## Slide 16: Critical Targets
Temperature
Under 40° Celsius
Size
< 30% Volume Increase
Puncture
110 MPa

## Slide 17: Critical Targets
Long Lasting
10 years
Weight
20% module weight
Pressure Loss
1 kPa

## Slide 18: Initial Design: Cooling Pipes around Inner wall of Module
Coolant Channel
Coolant inlet and outlet
Coolant channels fit within module walls

## Slide 19
Initial Design
Revised Design

## Slide 20: Pressure Loss
Universiteit Brussel Research
Initial Coolant Channel
Flow Rate: 0.2 m/s
Channel Length: 1 m
Pressure loss: 475 pa
Optimized Coolant Channel
Flow Rate: 0.2 m/s
Channel Length: 0.75 m
Pressure loss: 350 pa

## Slide 21: Module Assembly

## Slide 22: Module Assembly
Inlet/Outlet Push to Connect Fittings
Pouch Cell
Cold Plate
Aluminum Module Housing

## Slide 23: Design Parameters
Dimension: 255x212x5 mm
Weight:
0.30 kg
Dimension: 290x216x50 mm
Weight:
4.72 kg
Cold Plate
Module

## Slide 24: Physical Prototype
Top Plate
Bottom Plate

## Slide 25: Physical Prototype
Inlet Connector
Outlet Connector
Thermocouple Connection
RTV Gasket Glue

## Slide 26: Physical Prototype
Assemble Cold Plate
Bottom Plate
Top Plate

## Slide 27: Materials Selection
12V 2 GPM PowerFLO Diaphragm Pump
½" Thick 12" x 12" Aluminum Plate
MAX6675 K-Type Thermocouple
Gasket Glue

## Slide 28: Materials Selection
Vinyl Tubing
3D Printer Silicone Heated Pad 120V 150W
3/8” OD Push to Connect Fittings

## Slide 29: Testing
Transient Test
Parameter Matching
Coolant will flow while heating pads are still gaining temperature.
Temperature, mass flow rate, and pressure loss will be found experimentally and be compared to simulation results.
Steady Test
Coolant will flow once heating pads reach steady temperature.

## Slide 30: Testing
Aluminum
Wood
Aluminum
Wood
Module Housing Material

## Slide 31: Testing Setup
1
2
3
4
1. Power Supply
2. Pump
3. Thermocouple using Arduino
4. Pressure Gauge
5. Heating pads inside module

## Slide 32
Test Results
Initial transient tests indicate 1.25 ˚C difference between inlet and outlet
Steady state results are still being interpreted
Further calibration on thermocouples needed
As testing progresses, different steady state methods will be used

## Slide 33: COMSOL Prototype

## Slide 34: COMSOL Prototype
Transient Simulation
Inlet Temperature
293 K (20°C)
Outlet Temperature
294.7 K (66.8°C)
1.7 ˚C Temperature Increase

## Slide 35: COMSOL Results
Simulation Parameters: 5 C-Rate
60 s
Our Design
Air Cooled
Max Cell Temperature:
35.8°C (309 K)
Max Cell Temperature:
41.9°C (315 K)
Cooling Increase: 17%

## Slide 36: COMSOL Results
Steady State Temperature
Transient Temperature
317 K (43.8°C)
306.5 K (33.4°C)

## Slide 37: COMSOL Results
Steady State Temperature
Transient Temperature
340 K (66.8°C)
308.5 K (35.5°C)

## Slide 38: Validation
Initial transient tests match with transient comsol simulations. Simulations show temperature target is reached.
Calculations show pressure loss is within 5% of 1 kpa limit.
Calculations show that cooling method is within the 20% of module weight target.
Size target was not met. An increase of 15mm in module height results in a 42% increase in module volume.
Aluminum will not corrode with right coolant, so long lasting target is inconclusive but strong indications that it would be met.
Critical Target
Temperature
Transient tests prove that temperature target is reached
Result
Pressure
Calculations show pressure loss is within 5% of the 1 kPa target
Weight
Cooling design weighed 0.9 kg, under 20% of module
Size
Increased module height 15 mm resulting in a volume increase of 42%
Long Lasting
Aluminum will not corrode with coolant but external factors can impact its quality, leading to inconclusive results

## Slide 39: What it all means
We are within 5% of most of our targets using a Nissan Leaf battery for a class 8 vehicle. Most importantly the temperature target is reached.

## Slide 40: Budget
Chart: T507 Budget Breakdown
| Raw Materials | Hardware | Tubing & Connections | Test Materials
 | 228.18 | 254.01 | 212.88 | 244.93
Chart: T507 Total Budget
| Total Spent | Total Unspent
 | 940 | 1060

## Slide 41: Conclusion
Test results show that the design was effective and hit critical goals
For this design to be implemented it would need to be scaled up
More accurate thermocouples and real pouches could give more accurate test results
State of the art methods should be considered

## Slide 42: Future Work
Finish COMSOL Simulations of Prototype
Complete Testing
Compare COMSOL to Test Results to Validate Simulations

## Slide 43
Thanks for listening
Anthony Vicary | Chris Carley | Clayton Carlson | Corey Kelley | Jacob Owens
Anthony Vicary
Chris Carley
Corey Kelley
Jacob Owens
Clayton Carlson

## Slide 44: References
Goutam, S., Nikolian, A., Jaguemont, J., Smekens, J., Omar, N., Van Dan Bossche, P., & Van Mierlo, J. (2017). Three-dimensional electro-thermal model of li-ion pouch cell: Analysis and comparison of cell design factors and model assumptions. Applied Thermal Engineering, 126, 796–808. https://doi.org/10.1016/j.applthermaleng.2017.07.206

## Slide 46: Backup Slides

## Slide 47: Physical Prototype

## Slide 48: Physical Prototype

## Slide 49: Budget Breakdown Sheet
Raw Materials | Hardware | Tubing & Connections | Test Materials
$228.18 | $254.01 | $127.06 | $212.79

## Slide 50: Total Spent Sheet
Total Spent | Total Unspent
$822.06 | $1,177.94

## Slide 51: Raw Materials Table
Raw Materials |  |  |  |  | 
Item | Part Description | Quantity | Unit Cost | Total Cost | Category Cost
1 | Aluminum Plate 6061: T6511, 12 in Overall Lg, 10 in Overall Wd, 0.5 in Thick, Mill, +/-0.009 in, B95 | 2 | $50.49 | $100.98 | $228.18
2 | Aluminum Plate 6061: T6511, 12 in Overall Lg, 12 in Overall Wd, 0.5 in Thick, Mill, +/-0.009 in, B95 | 2 | $63.60 | $127.20 | 

## Slide 52: Hardware Table
Hardware |  |  |  |  | 
Item | Part Description | Quantity | Unit Cost | Total Cost | Category Cost
1 | 2Pcs Silicone Car Engine Heater Pad - 4" x 5" Self-Adhesive Oil Pan Heater Pad with 194°F Thermal Protector, 120V 150W Car Battery Warmer Pad Engine Block Heater Pad with 68" Long Power Cord (Orange) | 2 | $20.99 | $41.98 | $254.01
2 | BCZAMD 120V 500W Silicone Heating Pad 235 X 235mm Rubber Heater Mat with NTC 100K Thermistor Strong Adhesive for Crealit Ender 3 V2 3S Ender 5 3D Printer Heated Bed | 3 | $35.99 | $107.97 | 
3 | 12V 2 GPM PowerFLO Automatic Demand Diaphragm Pump | 1 | $87.07 | $87.07 | 
4 | 4 Sets DC 3-5V MAX6675 Thermocouple Module and K Type Thermocouple Temperature Sensor Thermocouple Sensor Set M6 Screw with Cable Cord Compatible with Arduino Raspberry Pi | 1 | $16.99 | $16.99 | 

## Slide 53: Tubing & Connections Table
Tubing & Connections |  |  |  |  | 
Item | Part Description | Quantity | Unit Cost | Total Cost | Order Cost
1 | 25 ft long Nylon Hose | 1 | $58.29 | $58.29 | $127.06
2 | Brass Barbed Hose Fitting for Air and Water Straight Adapter for 5/16" Hose ID, 3/8 NPTF Male | 1 | $18.95 | $18.95 | 
3 | Push-to-Connect Tube Fitting with Universal Thread for Air and Water, Adapter, 3/8" Tube OD x 1/4 Pipe | 6 | $3.65 | $21.90 | 
4 | Shark Industrial Premium Stainless Steel Dishwasher Hose - 10 FT No-Lead Burst Proof Water Supply Line 3/8" comp x 3/8" comp with attached 90 degree 3/8" comp x 3/8" MIP elbow - 10 year warranty | 1 | $12.95 | $12.95 | 
5 | 1/4 in. - 3/8 in. Tubing Bender | 1 | $14.97 | $14.97 | 

## Slide 54: Testing Materials Table
Test Materials |  |  |  |  | 
Item | Part Description | Quantity | Unit Cost | Total Cost | Order Cost
1 | Ultra Black® Oil Resistant RTV Silicone Gasket Maker, 3.35 Tube | 2 | $14.38 | $28.76 | $212.79
2 | Prestone DEX-COOL Antifreeze+Coolant; Extended Life -1 Gal- Ready to Use, 50/50 | 2.00 | $22.20 | $44.40 | 
3 | Great Value Aluminum Foil, 225 sq ft | 9 | $10.63 | $95.67 | 
4 | Rubbermaid Commercial Products 2.5 Gallon Brute Heavy-Duty, Corrosive-Resistant, Round Bucket, Red FG296300RED | 2 | $21.98 | $43.96 |