## Slide 1
1
NASA-MSFC Measurement of Cryogenic Propellant Fuel Levels
Team 516

## Slide 2: Team Introductions
Dane Seal
Design Engineer
Catherine Potts
Manufacturing Engineer
Team Introductions
Bryson Peters
Fluids Engineer
Zafer Jesri
Systems Engineer
Trevor Lay
Thermal Engineer
Bryson Peters

## Slide 3: Sponsor and Advisor
Engineering Mentor
Juan Valenzuela
Aerospace Engineer
Academic Advisor
Mark Vanderlaan, Ph.D.
Head of Hybrid and Cryogenics Operations
Sponsor
National Aeronautics and Space Association
(NASA)
Bryson Peters

## Slide 4: Project Objective
Create a support structure for a fiberoptic cable to measure cryogenic propellant levels in space.
Bryson Peters
4

## Slide 5: Background: Cryogenic Behavior in Space
Bryson Peters
5
Storage Tank
Liquid Fuel
Boil-off

## Slide 6: Background: Cryogenic Behavior in Space
Bryson Peters
Gas forms a thin layer along inside wall.

## Slide 7: Background: Cryogenic Behavior in Space
Bryson Peters
Gas bubbles congregate in center of tank.

## Slide 8: Background: Fiber Optic Sensing System
Bragg sensors read the strain on the fiber optic cable
8
Strain varies with temperature
The cable is connected to information system to relay data
Bryson Peters

## Slide 9: Background: Previous Designs
9
Bryson Peters

## Slide 10: Background: Previous Designs
10
Bryson Peters
Pulleys were used to guide the cable through the tank.
The cable would snap from stress concentration.

## Slide 11: Background: Previous Designs
Design by Team 514 (2021)
11
Rings hold cable with
minimal strain
Structure allowed for
twisting
No depth into center
of tank
Helical shape for the cable
Bryson Peters

## Slide 12: Customer Needs
Scalable Geometry
No Breakage at Cryogenic Temperatures
Measures Fuel Levels
Interpret Sensor Readings
12
Bryson Peters

## Slide 13: Design Specifications
13
Design can be scaled to operate in tank of 17 m3 (~600 ft3)
Base is no wider than 12 in
No taller than
18 in
Bryson Peters

## Slide 14: High Fidelity Concepts
14
Concentric Helical Sweep Concept
Honeycomb Support Concept
Triangular Truss Concept
Bryson Peters

## Slide 15: Concept Selection
15
Concentric Helical Sweep Concept
Honeycomb Support Concept
Triangular Truss Concept
Bryson Peters

## Slide 16: Concept Selection
16
Concentric Helical Sweep Concept
Honeycomb Support Concept
Triangular Truss Concept
Bryson Peters
Binary
Pairwise
Comparison
House
Of
Quality
Pugh
Chart
Analytical Hierarchy Process
Final
Selection

## Slide 17: Concept Selection
17
Concentric Helical Sweep Concept
Honeycomb Support Concept
Triangular Truss Concept
Bryson Peters
Concentric Helical Sweep Concept

## Slide 18: Final Selection
18
Nested helical sweeps of the cable
Located in the center of the tank
Increased structural stability
Attaching the support system to the dewar
Ensuring proper measurements are taken
Complications with open-dewar testing
Bryson Peters

## Slide 19: CAD Prototype
FOSS Hooks
Connector Rods
Outer Support Rings
Stabilizing Rods
Inner Support Rings
19
Trevor Lay

## Slide 20: CAD Parts
12 in
2 in
3 in
1.5 in
1 in
1 in
ϴ = 12 in
ϴ = 10 in
ϴ = 6 in
ϴ = 8 in
Thickness = 1 in
20
ϴ = 1 in
Thickness = 1 in
Trevor Lay

## Slide 21: Necessary Steps
G-10 has been ordered through Fastenal
Vacuum sealing to be done at the MagLab
Special machining tools need to be ordered
21
Trevor Lay

## Slide 22: Machining
22
Trevor Lay
ASE machine shop
Eight support rods from two 4ft rods
Eight connecting rods from one 2ft rod
Support rings from G-10 sheets

## Slide 23: Dewar
23
Dane Seal
Provided by MagLab
Dimension constraints: 14 in x 19 in
Liquid nitrogen will be provided

## Slide 24: Testing Procedure: Mass Gauging
24
Lower prototype into dewar
Read FOSS sensors and scale readings to check accuracy
Remove prototype and let liquid nitrogen evaporate
Fill dewar with liquid nitrogen
(~20 )
Place dewar on scale for weight readings
Dane Seal

## Slide 25
LN2
TESTING DEWAR
Temp = 77 K
Testing Procedure

## Slide 26: Budget
Dane Seal
Expended:
G-10 for Prototype
Shipping
Epoxy
Machining Tools
Total: $2,000
$1453.82
$546.18
Remaining:

## Slide 27: Current Work
Verify testing procedure
Visit NASA to receive feedback
Create CAD drawings for machine shop
Update website to illustrate
design and progress
27
Dane Seal

## Slide 28
Future Work
​Engineering Design Day (April 6)
28
​Prototype Assembly
​Testing
Prototype
Analyze Results
​Final
Design
Dane Seal

## Slide 29
Summary
29
Dane Seal

## Slide 30
Summary
The objective of our project is to create a support structure for a fiber optic cable to measure cryogenic
propellant levels in space
30
Dane Seal

## Slide 31
Summary
In space, cryogenic boil-off congregates in the center of the tank as non-viable fuel.
31
Dane Seal

## Slide 32
Summary
Our design must ensure no breakage at cryogenic temperatures. It must also be scalable and give an accurate fuel level reading
32
Dane Seal

## Slide 33
Summary
Our design features a double helix support system made of G-10 that carries the FOSS through the tank.
33
Dane Seal

## Slide 34
Summary
Mass Gauging: Compare the FOSS and scale readings to determine accuracy of preliminary design.
34
Dane Seal

## Slide 35
Summary
Finalizing the testing procedures and assembling the prototype are the next big steps
35
Dane Seal

## Slide 36
Life-Long Learning
Time Management
Flexibility
Communication
Dane Seal

## Slide 37
Backup Slides

## Slide 38
38
Life-Long Learning
Communication
Effective communication between teammates, advisors, professors, and sponsors are paramount for project success.
Time Management
Planning ahead and following a schedule allows for the project to be completed efficiently.
Flexibility
Ability to pivot quickly when mistakes or changes occur in the project or group.

## Slide 39: Project Objective
Create a support structure for a fiberoptic cable to measure cryogenic propellant levels in space.
Bryson Peters

## Slide 40
Assumptions
Testing will occur at the MAGLAB
Utilizing a dewar with liquid Nitrogen cryogenic testing fuel
Our structure will operate under zero-gravity conditions
The FOSS software is accurate and functional
Project Scope
Catherine Potts
40

## Slide 41: Functional Decomposition
Sensors
Structure
Power Source
Display Interface and Code
41
Presenter Name

## Slide 42
Targets and Metrics
Sensors
Structure
POWER
Display
We must ensure that the stress and strain incurred by the material at 77 K is not more than the material bounds.
Power source
supplies at least 12V​
The critical target dealing with the measurement system is the prevention of snapping or fracturing while exposed to LN2.
The critical target for the display aspect is ensuring that our values are presented in a recognizable and presentable manner.
42
Bryson Peters
Notes: Target max stress and strain values for glass: 1KN/area, 3.5% strain

## Slide 43
Brainstorm
Crap Shoot
Biomimicry
Concept Generation
S.C.A.M.P.E.R.
Catherine Potts
43

## Slide 44: VDR3 Prototype
Constructed using wooden dowels, staples, string, and super glue
Made to represent our concept visually
Next prototype will be made using G-10
44
Trevor Lay

## Slide 45: Design Challenges
Dewar dimensions and constraints
Altering design to better fit FOSS cable
Machining
(drill bits and material)
Zafer Jesri

## Slide 46: MagLab Safety Training
Cryogenic
Safety
Electrical
Safety
Hazard
Communication
Magnetic Field Safety
Zafer Jesri

## Slide 47: Functional Decomp Backup

## Slide 48
​Engineering Design Day
​Prototype Assembly
​Testing
Prototype
NASA MSFC Feedback
​Final
Design
​Order parts through certified vendors. Machine materials and parts to proper sizing. Assemble a testable prototype.
​Transfer prototype to MagLab for testing. Test the structure and FOSS system using test procedure discussed in Risk Assessment.
​Use the feedback provided from the trip to construct the best testing and assembly procedure.
​Develop final prototype based off initial results from testing. Test the new prototype to confirm optimal design.
​Present final design to NASA and other colleagues at the Engineering Design Day Fair.
​April 6
​April 1
​February 28
​March 6
​March 10

## Slide 49: Concept Selection Backup

## Slide 50: Detailed Math Backup

## Slide 51: Standard Shapes
Summary Box
Text box 1
Outlined Text Box

## Slide 52
52
Name
Do we still want this slide? Or nah

## Slide 53: Cool Shapes
Top View
Cable
Support Structure

## Slide 54: NASA-MSFC Measurement of Cryogenic Propellant Fuel Levels
Team 516
54

## Slide 55
55
NASA-MSFC Measurement of Cryogenic Propellant Fuel Levels​
Team 516

## Slide 56: Approved Logos

## Slide 57: Color Palette

## Slide 58: APA Tables
Category 1 | Category 2 | Category 3 | Category 4 | Category 5
Item 1 |  |  |  | 
Item 2 |  |  |  | 
Item 3 |  |  |  | 
Item 4 |  |  |  | 
 | Category 2 |  |  | Category 3 | 
Category 1 | subcategory 1 | subcategory 2 |  | subcategory 1 | subcategory 2
Item 1 |  |  |  |  | 
Item 2 |  |  |  |  | 
Item 3 |  |  |  |  | 
Item 4 |  |  |  |  |