## Slide 1: Full-Scale Test Flight 2
Launched again on February 24th.
  Added custom vinyl decals.
  Pressure ports
  Extra shear pin
  Accounted for weight and Cd in simulations
  Nosecone finish
Predicted flight
  Apogee: 4331-ft.
  Main Deploy: 600-ft.
Nicholas Hux

## Slide 2: Full-Scale Test Flight 2 Launch Video
Nicholas Hux

## Slide 3: Full-Scale Test Flight 2 Recovery Video
Nicholas Hux

## Slide 4: Full-Scale Test Flight 2 - Data
Both altimeters read apogee of 4493-ft.
Separation of airframe occurred as planned.
  Changes from last flight were successful.
Nicholas Hux
Notes: Fixes worked, but a new problem arose

## Slide 5: Full-Scale Test Flight 2
Failure Analysis
  Main parachute did not fully extend.
  Fin broke due to high kinetic energy upon impact.
Failure occurred through over-taping the parachute, and collision with avionics bay
Nicholas Hux