## Slide 1: Danfoss-Mini TT Shaft Bearing Press
Team 512
April 4, 2024

## Slide 2: Team Introductions
Clark Cooley
Systems Engineer
Brent Mynard
CAD Engineer
Cassie Bentley
Research Engineer
Colby Gullo
Safety Engineer

## Slide 3: Sponsors
Engineering Mentor
William Bilbow
Point of Contact & Sponsor
Engineering Mentor
Kevin Lohman
Sponsor

## Slide 4
Shaft Bearing Press Process
The bearing is heated then placed on the baseplate.
The shaft is placed on chuck then is lowered down.
Shaft is then pressed onto the bearing for a set time.
The bearing is heated to 600 degrees Fahrenheit then placed on the baseplate. ​
The shaft is then placed on the chuck and make sure it is securely fastened.​
The shaft is then pressed onto the bearing for a set amount of time.​
​

## Slide 5
The objective of this project is to redesign the existing bearing press to press bearings of various sizes onto shafts, while ensuring ease of manipulation and user safety.
Objective

## Slide 6: Project Background
Previous Shaft
Length: 5.6 inch
Updated Shaft
Length: 7.5 inch

## Slide 7: Original Design
The original press had several limitations that prevented it from usage.
Press Issues:
Not enough room for new shafts and new bearing housing.
Ineffective cage to protect operator.
Press could operate if door is open.
Original Design

## Slide 8: Key Goals
Height
Adjustability
Press Bearing On Shaft Stud
Ensure Safety Of User
Allow User Ease Of Usage
Optimize Cost

## Slide 9
SIZE
PRESSURE
SAFETY
Targets & Metrics

## Slide 10: Sponsor Preferences
Sponsor Preferences | Explanation
 | No "H" frame
 | Made in the USA
 | Pneumatic

## Slide 11: Research & Vendor Communication
We researched presses made in the USA to meet our key goals, evaluating based on cost-effectiveness, features, reputation, and reliability. From our findings, we selected a top three for consideration and recommend one standout option based on our sponsor’s preferences.

## Slide 12: Research & Vendor Communication
We researched presses made in the USA to meet our key goals, evaluating based on cost-effectiveness, features, reputation, and reliability. From our findings, we selected a top three for consideration and recommend one standout option based on our sponsor’s preferences.

## Slide 13
Press Selection Process
 | 6 Tons | 10 Tons | 20 Tons
Pneumatic | $21,032 |  | 
Hybrid |  | $37,567 | 
Hydraulic |  |  | $16,500

## Slide 14: Press Selection
Electric / Hydraulic operation provides smooth, consistent pressing action
Additive Features-Front safety guard for operator protection.
All hydraulic and mechanical parts are standard in the industry, and available throughout North America.
20 Tons
Key Features :
Found a viable press that Danfoss will order in 2025.

## Slide 15: Budget Optimization
Unable to make capital purchase
Fulfill the immediate need
Modify the existing press to meet the targets

## Slide 16: Optimizing the existing press
April 4, 2024
Clark Cooley

## Slide 17
Existing Constraints

## Slide 18
Actuator
2 stage 6-ton pneumatic cylinder
Operates at 100 psi (Danfoss standard air compression)
Only outputs 3300 pounds of pressure @ 100 psi

## Slide 19
Hardware
Hex bolts are kept to allow the new side panels to fit with the existing press plates.
The nylon tubing was used because it fit with the valves and actuator.
The Actuator is OSHA certified and fits with Danfoss Standards.

## Slide 20
20
Clark Cooley
Pneumatic Diagram
2 Stage Cylinder
Chuck
2 Hand Operator
Air Valve
Compressed Air

## Slide 21
21
Clark Cooley
Pneumatic Diagram
2 Stage Cylinder
Chuck
2 Hand Operator
Air Valve
Compressed Air
100 PSI

## Slide 22
22
Clark Cooley
Pneumatic Diagram
2 Stage Cylinder
Chuck
2 Hand Operator
Air Valve
Compressed Air
100 PSI
Extension
Retraction

## Slide 23
23
Clark Cooley
Pneumatic Diagram
2 Stage Cylinder
Chuck
2 Hand Operator
Air Valve
Compressed Air
100 PSI
Extension
Output

## Slide 24
24
Clark Cooley
Pneumatic Diagram
2 Stage Cylinder
Chuck
2 Hand Operator
Air Valve
Compressed Air
100 PSI
Retraction

## Slide 25
25
Clark Cooley
Pneumatic Diagram
2 Stage Cylinder
Chuck
2 Hand Operator
Air Valve
Compressed Air
100 PSI
Extension
Retraction

## Slide 26: CAD Modeling: New Design
Improvements:
Increased height on side walls
Increased C-shape depth & height for better baseplate support
Additional slots for actuator plate

## Slide 27: CAD Modeling: New Design
Height: 24 in (610 mm)
Width: 10 in (254 mm)
Depth: 12 in (305 mm)

## Slide 28
Structural Improvements
4 pairs of pin holes & slots for various heights
3 pairs of pin holes & slots for various heights
New Design
Original Design
VS

## Slide 29
Structural Improvements
Dimensions:
Height: 4.9 ~ 5.6 in
Diameter: 3.9 in
Stroke: 7 inch
Daylight: 14.5 inch
(With chuck: 12.7 inch)
New Design
Original Design
VS
Stroke: 7 inch
Daylight: 10.5 inch
(With chuck: 8.7 inch)

## Slide 30: Material Selection
April 4, 2024
Brent Mynard

## Slide 31
Stress Analysis: Equations
Stress Test Equation
Hooke's Law
Pressure: 100 PSI (Max)
Force Output: 3282.73638 lbs. (Max)
Actuator output area: 38.4846 inch2 (24828.7245 mm2)
Applied baseplate area: 60 inch2 (38710 mm2)
Applied actuator plate area: 81.6 inch2 (52645.056 mm2)

## Slide 32
Stress Analysis: Results
21.001 MPa
18.668 MPa
16.334 MPa
14.001 MPa
11.667 MPa
9.334 MPa
7.0005 MPa
4.667 MPa
2.3335 MPa
8.4166e-7 MPa
MAX
MIN
24.558 MPa
4140 Steel
1018 Steel

## Slide 33
0.05259 mm
0.046746 mm
0.040903 mm
0.03506 mm
0.029217 mm
0.023373 mm
0.01753 mm
0.011687 mm
0.0058433 mm
0.0 mm
MAX
MIN
0.05998 mm
1018 Steel
4140 Steel
Deformation Analysis: Results

## Slide 34
Material Selection
To prevent any delays, it was decided to agree on a design first before doing stress and deformation analyses.
1018 Steel | 4140 Steel
1018 steel is easier to machine compared to 4140 steel. | 
 | 4140 steel can be heat-treated to achieve higher hardness levels, enhancing its wear resistance and durability.
1018 steel is commonly stocked by many suppliers and readily available in various forms and sizes. | 
12 x 24 x ¾ in Sheet: $340 | 12 x 24 x ¾ in Sheet: $993

## Slide 35
Material Selection
To prevent any delays, it was decided to agree on a design first before doing stress and deformation analyses.
1018 Steel | 4140 Steel
1018 steel is easier to machine compared to 4140 steel. | 
 | 4140 steel can be heat-treated to achieve higher hardness levels, enhancing its wear resistance and durability.
1018 steel is commonly stocked by many suppliers and readily available in various forms and sizes. | 
12 x 24 x ¾ in Sheet: $340 | 12 x 24 x ¾ in Sheet: $993

## Slide 36
Cage Design
Width: 24 inch
Height: 24 inch
Depth: 19 inch
Bar Thickness: 1 inch

## Slide 37
Cage Design
Improvements:
Stronger Material
Pneumatic Lock Incorporation
Improved Ventilation

## Slide 38: Final Product
Allows for faster cooling of press and parts
May be electrical

## Slide 39
Assessing Design Options
Early design idea: Optional slots below the chuck and integrated cage on press frame
Provided a fix to both the daylight amount and a better cage
Reasons for failure (don’t say this):
Complex design and assembly.
Not enough room for operator’s hands to place the bearing housing.
Actuator with chuck and new shafts were not long enough to reach the bearing housing.

## Slide 40: Press Features
April 4, 2024
Brent Mynard

## Slide 41: Future Press Features
Keeping The Press Pneumatic

## Slide 42: Future Press Features
Should only activate when press is in use
Must recognize when door is open or closed

## Slide 43: Future Press Features
Keeping The Press Pneumatic

## Slide 44
Emergency stop must immediately stop all actions
Must override timer
No exceptions
Future Work: Emergency Stop

## Slide 45: Future Press Features
Keeping The Press Pneumatic

## Slide 46: Future Work: Pneumatic Timer
Allows press to continue applying force for set time after actuator is released
Able to be overridden by emergency stop

## Slide 47: Future Press Features
Keeping The Press Pneumatic

## Slide 48: Feature: Fan
Decreases heat caused by convection currents
Can be electrical

## Slide 49
49
Colby Gullo
Modified Press Pneumatic Diagram
2 Stage Cylinder
Chuck
2 Hand Operator
Air Valve
Compressed Air
E-Stop
Pneumatic lock

## Slide 50: Budget
Chart: $10,000 Initial Budget
| Sidewalls | Cage | Leftover for Future Press
$10,000 Budget | 800 | 500 | 8700

## Slide 51: Future Work
Safety Guard
Final Tests
Deliver To Danfoss

## Slide 52: Project Recap
SIZE
PRESSURE
SAFETY
Cassie Bentley
52
Height
Adjustability
Press Bearing On Shaft Stud
Ensure Safety Of User
Allow User Ease Of Usage
Optimize Cost
​Targets and Metrics
​Key Goals
​TBD

## Slide 53: Lessons Learned As A Team
Provide Various Alternatives To The Sponsor
Be Prepared For Setbacks
Have Good Organization
Maintain Consistent Communication

## Slide 54: Thank You

## Slide 55: Backup Slides

## Slide 56: Slides we are not using …....

## Slide 57: Original Design
The original press had several limitations that prevented it from usage.
CAD Issues:
Not enough room for new shafts and new bearing housing.
Ineffective cage to protect operator.
Original Design

## Slide 58: CAD Modeling: Original Design
The original press had several limitations that prevented it from usage.
CAD Issues:
Not enough room for new shafts and new bearing housing.
Ineffective cage to protect operator.
Original Design

## Slide 59: Fall Semester
Current Press

## Slide 60: Fall Semester
Providing Regular Updates: Describe how you maintained regular communication with the sponsor, keeping them informed about project progress, milestones achieved, and any potential issues encountered.
Problems:
The current press won't fit the new shaft size
The plexiglass is a safety concern
Press should not operate if door is open

## Slide 61: Fall Semester
Providing Regular Updates: Describe how you maintained regular communication with the sponsor, keeping them informed about project progress, milestones achieved, and any potential issues encountered.
Problems:
The current press won't fit the new shaft size
The plexiglass is a safety concern
Press should not operate if door is open

## Slide 62: Fall Semester
Providing Regular Updates: Describe how you maintained regular communication with the sponsor, keeping them informed about project progress, milestones achieved, and any potential issues encountered.
Problems:
The current press won't fit the new shaft size
The plexiglass is a safety concern
Press should not operate if door is open

## Slide 63: Fall Semester
Providing Regular Updates: Describe how you maintained regular communication with the sponsor, keeping them informed about project progress, milestones achieved, and any potential issues encountered.
Problems:
The current press won't fit the new shaft size
The plexiglass is a safety concern
Press should not operate if door is open

## Slide 64: Fall Semester
Find A Press:
Conduct research on various vendors and work closely with our sponsor to comprehend the project's requirements, desires, and financial constraint

## Slide 65: Sponsor Communication
Post-Order Adjustments:
After placing the order for the press, we will proceed to make necessary adjustments that were not included with the press to ensure it meets the sponsor's preferences and enhances safety.

## Slide 66: CAD Modeling: Original Design
The original press had several limitations that prevented it from usage.
CAD Issues:
Not enough room for new shafts and new bearing housing.
Ineffective cage to protect operator.
Original Design

## Slide 67
Bearing Housing
Dimensions:
Height: 4.9 ~ 5.6 in
Diameter: 3.9 in
Purpose:
Holds the bearing during pressing
Accommodates the different shafts
*This slide is to show our process in finding the height for press. I believe these are covered by NDA, so maybe cover pic/dimensions

## Slide 68: Team Coordination
Team Lead: Led team in conducting meetings between the sponsor and team.
Systems engineer: Facilitated the design of the new press while salvaging components from the old press and working under budget constraints
Cage design: Communicated with the fabricator and aided with the design of the new cage and lock.
Pneumatic system: Aided in the Design of the pneumatic system and logic of converting compressed air to a pneumatic press.

## Slide 69: Current Semester: Milestone Updates
Old Press Design

## Slide 70: Old Design
6 ” stroke
8 ” clearance
2” chuck

## Slide 71: Current Semester: Milestone Updates
New Press Design

## Slide 72: Pneumatic Components
Two-Handed Actuator
Emergency Stop
Pneumatic Timer
Door Sensor/Lock
Air Cylinder

## Slide 73: Current Semester: Milestone Updates
New Press Design

## Slide 74: CAD Modeling
Original Design
The original press was measured, and CAD drawings were acquired from the manufacturer. From there, the sponsor’s needs were taken in, and a new design was created over several iterations.
New Design

## Slide 75
Structural Design
Dimensions:
Height: 4.9 ~ 5.6 in
Diameter: 3.9 in
Stroke 7"
Daylight: 13 inch
(With chuck: 12.7 inch)
Throat
Bearing housing 5.6"
Clearance between shaft end and bearing housing 1"

## Slide 76: New Design
6 ” stroke
12 ” clearance
2 - 2 ” chuck
1 ” between new bearing and shaft

## Slide 77
This is 10-point
This is 15–point Times
This is 20–point
This is 25–point
This is 30–point
This is 35–point
This is 40–point
This is 50–point
This is 60–point
This is 72–point
Notes: Use at least 20-point font in Room A105, B134, and B136
Use at least 25-point font in Room B135

## Slide 78: College of Engineering Color Palette
Fang
Orange
RGB: 238, 118, 36
Hex: #EE7624
CMYK:2, 66, 99, 0
1 2 3 4
1 2 3 4
White
Pantone: PMS 000C
RGB: 255, 255, 255
Hex: #FFFFFF
CMYK: 0, 0, 0, 0
1 2 3 4
Black
Pantone: Black C
RGB: 0, 0, 0
Hex: #000000
CMYK:0, 0, 0, 100
Garnet
Pantone: PMS 195 C
RGB: 120, 47, 64
Hex: #782F40
CMYK:19, 90, 50, 55
1 2 3 4
Notes: Avoid 75% Black in B135

## Slide 79: Accent Color Palette
1 2 3 4
Tardis Blue
RGB: 0, 59, 111
Hex: #003B6F
CMYK:
1 2 3 4
Turquoise
RGB: 64, 224, 208
Hex: #40E0D0
CMYK:
1 2 3 4
American Orange
RGB: 255, 139, 0
Hex: #FF8B00
CMYK:
Rubine Red
RGB: 206, 0, 88
Hex: #CE0058
CMYK: 0, 100, 43, 12
1 2 3 4
1 2 3 4
Asagi-iro
RGB: 72, 146, 155
Hex: #48929b
CMYK:
1 2 3 4
Gainsboro
RGB: 220, 220, 220
Hex: #DCDCDC
CMYK:
1 2 3 4
Corn
RGB: 251, 236, 93
Hex: #FBEC5D
CMYK:
1 2 3 4
Timberwolf
RGB: 219, 215, 210
Hex: #DBD7D2
CMYK:
Imperial
RGB: 104, 40, 96
Hex: #682860
CMYK:
1 2 3 4
1 2 3 4
Tardis Blue
RGB: 0, 59, 111
Hex: #003B6F
CMYK:
Rubine Red
RGB: 206, 0, 88
Hex: #CE0058
CMYK: 0, 100, 43, 12
1 2 3 4
1 2 3 4
Corn
RGB: 251, 236, 93
Hex: #FBEC5D
CMYK:
1 2 3 4
Timberwolf
RGB: 219, 215, 210
Hex: #DBD7D2
CMYK:
Notes: Remove American orange add hyperlink grey
Make corn the last for b135
All work in 134 imperial move later
Tardis doesn’t work in b136

## Slide 80
https://color.adobe.com/create/color-wheel
Analogous
F7AB19
D67F15
EE7624
D64615
F73119
Monochromatic
6E3610
F0A16C
EE7624
6E4931
BASB1C
Triad
A14508
4BED3B
EE7624
250CED
2010A1
Complementary
FF8C40
EE7624
0098A1
24E2ED
A1470C
Split Complementary
28A164
2FED8D
EE7624
0848A1
1871ED
Double Split Complementary
3BED93
EE7624
0C6AED
ED2F18
EDAC2F
Square
C7ED3B
EE7624
0CE1ED
A418ED
ED660C
Compound
87724A
EE7624
60EFCF
09BA61
BA7E09
Shades
6E3610
EE7624
FA7625
D46820
AD551A
Notes: These are the variants that work well with Fang Orange. The bolded items show well on the projectors.

## Slide 81
https://color.adobe.com/create/color-wheel
Analogous
85412D
8F3831
782f40
8F3176
792D85
Monochromatic
C44D69
8E626D
782F40
C48796
451B25
Triad
C43959
78743B
782F40
236178
43A2C4
Complementary
C46078
782F40
25C43D
2F783A
C43959
Split Complementary
93C460
577835
782F40
39C49D
297861
Double Split Complementary
5A783B
782F40
237860
6E2978
784435
Square
78683b
782F40
237830
293978
782337
Compound
DEBAAF
782F40
5D8555
70AB32
AB4D32
Shades
C44D69
782F40
853447
5E2532
38161E

## Slide 82
B135 Stage Right
A105
A105
B135 Stage Left
B135
B134, A105
B136